## Slide 1: Ensemble and Variational Data Assimilation for the Storm Scale and with GSI for Rapid Refresh
Ming Xue
Center for Analysis and Prediction of Storms (CAPS)
and School of Meteorology
University of Oklahoma
mxue@ou.edu
October 2014
Given at the EMC/NCEP
ARPS Simulated Tornado

## Slide 2: Convective-Scale DA and Prediction
Here “Convective Scale” mainly refers to moist convection/storms, that require ~1 km grid spacing to resolve;
Need comparable-resolution observations to observe the convection itself, and other high-resolution observations to sample the storm environment;
Radar is the most important observation platform for the convective storms;

## Slide 3: Specific Challenges with Convective-Scale Data Assimilation
Radar observes very few parameters (Vr and Z), no coverage in clear air region;
Model constraint essential to ‘retrieve’ unobserved variables but model and state errors tend to be large;
Analysis very sensitive to model errors, especially for un-observed/retrieved parameters;
Need quality storm environment to support storm prediction – a multiscale/multi-data source problem;

## Slide 4: Specific Challenges with Convective-Scale Data Assimilation - continued
Much higher degree of freedom – more difficult for typical small-ensemble DA system to adequately sample essential directions to fit observations and retrieve unobserved quantities;
Strongly nonlinear physics a serious obstacle for adjoint-based 4DVAR methods; Single-moment microphysics may not be enough;
Ensemble system design/ensemble perturbation maintenance less well understood than larger-scale DA system;
Much larger computational challenges;

## Slide 5: Radial Velocity (Vr) Data
Most times, only single-Doppler radial velocity coverage is available;
Radial velocity observation operator:
Sometimes Vr is further weighted by reflectivity factors, making it microphysics dependent and more nonlinear.

## Slide 6: Reflectivity for Precipitating Hydrometeors
Assuming exponential DSD,
Equivalent reflectivity factor:
where is DSD slope
Ze in mm6/m3
qr, qs, qh in kg/kg
Smith, Meyer and Orville (1975), Tong and Xue (2005), Dowell et al. (2011)
Total reflectivity in dBZ:
Nonlinear!

## Slide 7: Within Convective Storms
From Vr and Z, we need to determine ≥16 state variables (when predicting two MP moments):
u, v, w, T, p, qc, qi, qv, qr, qs, qh/g, NTc, NTi, NTr, NTs, NTh/g, etc.
where NT is total number concentration.
The problem is severely under-determined!
3DVar by itself is incapable to analyzing so many variables - Need help from physical constraints, e.g., a numerical model.

## Slide 8: 3DVar Analysis of Hydrometeors at Surface from Z
Gao and Stensrud (2012)
Truth
Original Z operator
T-dependent operator

## Slide 9: Solutions
4DVar uses model equations as a strong constraint, and multi-time level data (e.g., VDRAS – warm rain only);
EnKF (EnSRF/EAKF/LETKF etc) uses model constraints in a statistical representation, and accumulates info in time;
3DVar for Vr and complex cloud analysis for Z (e.g., ARPS and RUC/RAP 3DVar systems with cloud analysis);
Methods that combine the above (EnVar, hyrid)
Polarimetric radar measurements may provide additional MP information.

## Slide 10: Solutions
4DVar uses model equations as a strong constraint, and multi-time level data (e.g., VDRAS – warm rain only);
EnKF (EnSRF/EAKF/LETKF etc) uses model constraints in a statistical representation, and accumulates info in time;
3DVar for Vr and complex cloud analysis for Z (e.g., ARPS and RUC/RAP 3DVar systems with cloud analysis);
Methods that combine the above (EnVar, hyrid)
Polarimetric radar measurements may provide additional MP information.

## Slide 11
        ARPS Complex Cloud Analysis
Construct 3D cloud fields using radar reflectivity data, surface cloud observations, satellite data, and the background from previous forecast by semi-empirical rules.
Retrieve hydrometeors and adjusts in-cloud temperature and moisture.
The increments can be applied as a single time or gradually through IAU (Incremental Analysis Update)

## Slide 12: ARPS Cloud Analysis
GOES Satellite Data Vis: Cloud fraction IR: Cloud top temperature
Radar Data Reflectivity to precipitation hydrometeors
Surface Observations Cloudbase height
Originated from the LAPS cloud analysis, with adaptation and updates by Jian Zhang and Keith Brewster, et al.
(also Xue et al. 2003 MAP, Hu et al. 2006 MWR)

## Slide 13: Estimating the Cloud Water
Use parcel theory to find saturation dqvsat/dz and increment cloud water
Water is carried with parcel - less a mixing/dilution factor (Warner curve)
Ice created when colder than –10 C
Cloud water/ice reduced in later step if precipitating hydrometeors are prescribed (presumed converted by coalescence or aggregation)

## Slide 14: In-cloud temperature adjustment (Diabatic Heating)
Original:
Updated:
  Moist-adiabatic temperature profile
  Warner entrainment curve
  Heating applied only in updraft regions

## Slide 15: Moisture adjustment
Adjusted to saturation within cloudy regions.
May be optionally applied to the first analysis cycle only.
Analysis increments may be applied incrementally via Incremental Analysis Update (IAU) to reduce shock.
Cloud analysis is typically combined with ADAS or 3DVAR (including Vr data)

## Slide 16: CAPS Realtime Storm-Scale Ensemble Forecasting for NOAA Hazardous Weather Testbed Spring Experiments
Realtime 4-km ensemble and 1-km deterministic forecasts over entire CONUS
Assimilating Level-2 Vr and Z data from all WSR-88D radars using ARPS 3DVAR/Cloud analysis since 2008
Initialize ARW-ARW, WRF-NMM and ARPS models.

## Slide 17: June 14, 2010 – Oklahoma City Flooding ~ 10 inch rain fell in part of OKC

## Slide 18: June 14, 2010 – Oklahoma City Flooding Case
Radar reflectivity observation 1 km CAPS realtime forecast using WRF
4640x2880x50 grid
Movie

## Slide 19: Equitable Threat Scores for 3-hourly Precip. ≥ 0.5 in
With radar
no radar
12 km NAM
2009 (26-day)
With radar
no radar
12 km NAM
2008 (32-day)
2010 (36-day)
Radar data impact lasts up to in 12 hours
All high-res models outperform 12km NAM
Probability-matched score generally better than any ensemble member
2 km score no-better than the best 4-km ensemble member – may be due to physics
1-km score better than any 4-km member and than the 4 km PM score in 2009.
With radar
no radar
12 km NAM
Notes: Probability-matched score generally better than any ensemble member
2 km score no-better than the best 4-km ensemble member – may be due to physics
1-km score better than any 4-km member and than the 4 km PM score.

## Slide 20: Limitations of 3DVAR/Cloud Analysis
Unobserved cross-beam wind components tend to be poor;
Microphysics and thermodynamic fields don’t fit model well  fast error growth;
General lack of balance among state variables;
Difficult to suppress spurious storms, more problematic with continuous cycling.

## Slide 21: Solutions
4DVar uses model equations as a strong constraint, and multi-time level data (e.g., VDRAS – warm rain only);
EnKF (EnSRF/EAKF/LETKF etc) uses model constraints in a statistical representation, and accumulates info in time;
3DVar for Vr and complex cloud analysis for Z (e.g., ARPS and RUC/RAP 3DVar systems with cloud analysis);
Methods that combine the above (EnVar, hyrid)
Polarimetric radar measurements may provide additional MP information.

## Slide 22: EnKF Assimilation of Vr and Z with Multi-Phase Microphysics (Tong and Xue 2005 MWR)
Radar data:
Vr only (Z>10dBZ)
Vr (Z>10dBZ) & Z
K is the Kalman Gain, a function
of background and obs error covariances
Tong, M. and M. Xue, 2005: Ensemble Kalman filter assimilation of Doppler radar data with a compressible nonhydrostatic model: OSS Experiments. Mon. Wea. Rev., 133, 1789-1807.

## Slide 23: Analyses of Low level cold pool and reflectivity v.s. Truth
Truth
Vr only
Vr + Z

## Slide 24: Analysis of Microphysical Fields
Vr only
Truth
Vr + Z
qc
qr
qi
qs
qh
Notes: qc, qr, qi, qs, qh at T=65 min

## Slide 25: Correlation coefficients between Z and model states at t=80min Experiment assimilating Z (>10dBZ) only
u
w
q’
P’
qc
qr
qs
qh

## Slide 26: Cross-covariances Critical
RMS ensemble mean forecast and analysis errors
Red: Only update variables directly involved in obs operators when assimilating Vr and Z

## Slide 27: Analysis and ensemble forecasting of a tornadic mesoscale convective system (MCS) based on EnKF assimilation of CASA X-band and WSR-88D radar data Snook, Xue and Jung (MWR 2011, 2012) Putnam et al. (2014)
Snook, N., M. Xue, and J. Jung, 2011: Analysis of a tornadic meoscale convective vortex based on ensemble Kalman filter assimilation of CASA X-band and WSR-88D radar data. Mon. Wea. Rev., 139, 3446-3468.
Snook, N., M. Xue, and Y. Jung, 2012: Ensemble probabilistic forecasts of a tornadic mesoscale convective system from ensemble Kalman filter analyses using WSR-88D and CASA radar data. Mon. Wea. Rev., 140, 2126-2146.
Putnam, B. J., M. Xue, Y. Jung, N. A. Snook, and G. Zhang, 2014: The analysis and prediction of microphysical states and polarimetric variables in a mesoscale convective system using double-moment microphysics, multi-network radar data, and the ensemble Kalman filter. Mon. Wea. Rev, 142, 141-162.

## Slide 28
© Patrick Marsh
7:21pm (0021Z) Lawton Tornado
Minco Tornado 10:54pm (0354Z)
Tornadoes of 8-9 May 2007
El Reno tornado
Lawton tornado
Union City tornado
CASA X-band Radar Network – 30 km range

## Slide 29: EnKF analysis and ensemble forecasts for May 8-9 2007 tornadic mesoscale convective system (MCS)
0:00Z
0:30Z
1:00Z
1:30Z
2:00Z
2:30Z
3:00Z
3:30Z
1 hr. spin-up period
4:00Z
Deterministic forecast
Ensemble forecast
4:30Z
5:00Z
Reported tornadoes 
Assimilation period
(Snook, Jung and Xue 2011; 2012, Putnam et al. 2014 MWR)
dx=2 km
Used multiple microphysics in ensemble
Notes: Experiment contained 40 Ensemble members. Reflectivity and radial velocity observations from 5 WSR-88D radars as well as the 4 CASA radars were assimilated every 5 minutes over a 1 hour window.
Analysis and probabilistic ensemble forecasts were generated for three experiments to test effect of assimilated CASA data and use of a mixed-microphysics ensemble using three single moment ice microphysics schemes.
2-moment (DM) of Milbrandt and Yau (2005) were used in both simulation and analysis and compared with the results using a 1-moment (mixed NEM, Lin, and WSM-6).The final analyses were used to initialize 1-moment and 2-moment 2 hour forecasts, respectively. This work is an extension of previous work by Snook et al. (2011) and Jung et al. (2010)

## Slide 30: Single- and Dual-Moment Microphysical State Estimation with EnKF Direct Comparison with Radar Reflectivity
Final analysis (0200 UTC ) Reflectivity
Two-hour forecast (0400 UTC)
OBS
SM
MY DM
(Putnam, et al. 2014 MWR)
Notes: The analyzed reflectivity fields in both 1-moment and 2-moment experiments compare well with radar observations (shown at top).
However, 2-moment forecast show significant improvement over the 1-moment experiment (shown at bottom).
The structure and evolution of the forecast MCS, LEV and leading and trailing convective lines is remarkably better with a 2-moment scheme throughout the forecast period than with a 1-moment scheme.
Putnam, B. J., M. Xue, Y. Jung, N. A. Snook, and G. Zhang, 2013: The analysis and prediction of microphysical states and polarimetric variables in a mesoscale convective system using double-moment microphysics, multi-network radar data, and the ensemble Kalman filter. Mon. Wea. Rev., In press.

## Slide 31
Two hour Forecast (0400 UTC)
KOUN OBS
1-moment
2-moment
Z
ZDR
KDP
Too high
Same
pattern
as Z –
No unique
info
Effects of
size sorting
Notes: Polarimetric variables on .5 tilt as seen by KOUN using polarimetric radar data simulator (Jung et al. 2010)
Size sorting of hydrometeors on the leading edge of the system indicated by increased ZDR. The reduction of ZDR in the center of the line in 2-moment experiment is due to hail while observations show no sign of hail.
KDP is unrealistically high in the 1-moment scheme (maximum ~ 11 deg/km), suggesting an excess of rain drops. As with ZDR , the 2-moment scheme values are also higher than observed, but the results are in a closer agreement with observations.

## Slide 32: 4D Ensemble Kalman Filter (4DEnKF/4DEnSRF)
Obs
t0
Obs
Obs
Obs
Obs
Obs
Obs
t1
One assimilation cycle
State updating
Phased array radars can provide fast volume scans
Wang, Xue and Min (2012 QJ)
Notes: The EnKF is a 4-d data-assimilation method that uses a Monte-Carlo
ensemble of short-range forecasts to estimate the covariances of the forecast
error (Evensen,1994).

## Slide 33: 4D Asynchronous EnSRF (4DEnSRF)
Motivation
  High-frequency EnKF DA is costly, given that data I/O can cost >80% overall (reading and writing of ensembles).
  4D extension of EnKF requires fewer cycles while still using obs at their correct times
  Implemented based on the serial EnSRF algorithm in the ARPS EnKF framework – 4DEnSRF
  Forecast model used was WRF-ARW.
Wang, Xue and Min (QJRMS 2012)

## Slide 34
ta: time of analysis, Δt: analysis time interval, to: time of observation
4DEnKF vs. Regular EnKF
EnKF: Observation are assumed to be taken at the assimilation time, like 3DVAR.
Δt
ta1
ta2
yo1
yo2
yo3
yo4
time
ta1
ta2
yo1
yo2
yo3
yo4
H(x)o1
H(x)o2
H(x)o3
H(x)o4
to1
to2
to3
to4
4DEnKF: Observation can be assimilated at the times they are taken – no timing error, like 4DVAR
Existing 4D ensemble algorithms include 4D-LETKF, En4DVAR.
4D EnSRF algorithm requires special treatment due to its serial nature.
4DEnSRF computes and update observation priors at the observations times.
4DEnSRF has been tested with simulated radar data for both WRF and ARPS, and with real data and ARPS.
H(x) can be calculated within the numerical model – added to ARPS.
to1
to2
to3
to4

## Slide 35: 4DEnSRF v.s. EnSRF with 5 min data batches
Reflectivity
Analyzed reflectivity with EnSRF exhibits larger errors due to timing error
Color shade: Truth Black contours: Analysis
EnSRF
4DEnSRF

## Slide 36: EnSRF and 4DEnSRF Analysis and Forecast Errors: OSSEs for a Supercell with WRF
Chart: 
| 23 | 23 | 28 | 28 | 33 | 33 | 38 | 38 | 43 | 43 | 48 | 48 | 53 | 53 | 58 | 58 | 63 | 63 | 68 | 68 | 73 | 73 | 78 | 78 | 83 | 83 | 88 | 88
stdu_exp2020
dte_exp2020_x2L6_ne | 9.3227 | 7.6313 | 7.8377 | 7.0093 | 4.9687 | 4.182 | 3.7463 | 3.1773 | 3.1081 | 2.5968 | 2.6805 | 2.2128 | 2.4218 | 2.0391 | 2.3962 | 1.9808 | 2.271 | 1.9113 | 2.293 | 1.9606 | 2.2008 | 1.8898 | 2.3771 | 1.94 | 2.4989 | 2.0449 | 2.5892 | 2.0963
stdu_exp2020_x2
dte_exp2021_x2L6_dt | 9.3227 | 7.55 | 6.6752 | 5.4631 | 3.8498 | 3.8158 | 3.3102 | 2.9782 | 2.7952 | 2.6268 | 2.9553 | 2.5215 | 3.0421 | 2.465 | 3.0174 | 2.6818 | 3.5714 | 2.8753 | 3.4375 | 2.7302 | 3.6703 | 3.0924 | 3.7434 | 3.0189 | 4.4897 | 3.7247 | 5.1932 | 4.1486
stdu_exp2021_x2



Chart: 
| 23 | 23 | 28 | 28 | 33 | 33 | 38 | 38 | 43 | 43 | 48 | 48 | 53 | 53 | 58 | 58 | 63 | 63 | 68 | 68 | 73 | 73 | 78 | 78 | 83 | 83 | 88 | 88
stdv_exp2020
rms_ref_exp2020_x2L | 1.8385 | 1.8209 | 1.9711 | 1.7048 | 1.1675 | 0.81654 | 0.67303 | 0.45088 | 0.5036 | 0.35068 | 0.44088 | 0.31728 | 0.35742 | 0.25857 | 0.32138 | 0.22805 | 0.27575 | 0.20749 | 0.27679 | 0.22389 | 0.29866 | 0.21534 | 0.30247 | 0.21652 | 0.30926 | 0.23879 | 0.32884 | 0.22729
stdv_exp2020_x2
rms_ref_exp2021_x2L | 1.8385 | 1.9342 | 1.4517 | 1.1573 | 0.80947 | 0.71931 | 0.64071 | 0.52047 | 0.49026 | 0.44582 | 0.51587 | 0.46406 | 0.52634 | 0.44204 | 0.49241 | 0.45304 | 0.46114 | 0.4329 | 0.47124 | 0.40657 | 0.49141 | 0.44771 | 0.50983 | 0.44401 | 0.57075 | 0.48774 | 0.63939 | 0.53712
stdv_exp2021_x2



Chart: 
| 22 | 22 | 25 | 25 | 28 | 28 | 31 | 31 | 34 | 34 | 37 | 37 | 40 | 40 | 43 | 43 | 46 | 46 | 49 | 49 | 52 | 52 | 55 | 55 | 58 | 58 | 61 | 61 | 64 | 64 | 67 | 67 | 70 | 70 | 73 | 73 | 76 | 76 | 79 | 79 | 82 | 82 | 85 | 85 | 88 | 88
stdu_exp2024
stdu_exp2024_x2
stdu_exp2025_x2
stdu_exp2025_1


Chart: 
| 22 | 22 | 25 | 25 | 28 | 28 | 31 | 31 | 34 | 34 | 37 | 37 | 40 | 40 | 43 | 43 | 46 | 46 | 49 | 49 | 52 | 52 | 55 | 55 | 58 | 58 | 61 | 61 | 64 | 64 | 67 | 67 | 70 | 70 | 73 | 73 | 76 | 76 | 79 | 79 | 82 | 82 | 85 | 85 | 88 | 88
stdv_exp2024
stdv_exp2024_x2
stdv_exp2025_x2
stdv_exp2025_1


Blue: EnSRF Red: 4DEnSRF
Chart: 
| 25 | 25 | 35 | 35 | 45 | 45 | 55 | 55 | 65 | 65 | 75 | 75 | 85 | 85
stdu_exp2026
dte_exp2026_x2L6_ne | 9.1469 | 7.8366 | 4.9434 | 4.2648 | 3.6398 | 2.6438 | 3.035 | 2.1704 | 3.0403 | 2.2089 | 2.8005 | 2.109 | 2.9114 | 2.1954
dte_exp2027_x2L6_dt | 9.1622 | 7.9352 | 6.3157 | 5.7651 | 4.6981 | 4.432 | 4.5861 | 4.66 | 4.4946 | 4.5945 | 5.1021 | 4.8097 | 6.1472 | 5.6527
stdu_exp2027_1


Chart: 
| 25 | 25 | 35 | 35 | 45 | 45 | 55 | 55 | 65 | 65 | 75 | 75 | 85 | 85
stdv_exp2026
rms_ref_exp2026_x2L | 1.9863 | 1.999 | 1.0231 | 0.85371 | 0.70442 | 0.41849 | 0.50757 | 0.32638 | 0.41823 | 0.28563 | 0.36186 | 0.25582 | 0.35286 | 0.23449
rms_ref_exp2027_x2L | 1.9861 | 2.2891 | 1.3771 | 1.0446 | 0.90466 | 0.73894 | 0.76163 | 0.65715 | 0.62907 | 0.66842 | 0.67175 | 0.69405 | 0.82361 | 0.7367
stdv_exp2027_1


Chart: 
| 22 | 22 | 25 | 25 | 28 | 28 | 31 | 31 | 34 | 34 | 37 | 37 | 40 | 40 | 43 | 43 | 46 | 46 | 49 | 49 | 52 | 52 | 55 | 55 | 58 | 58 | 61 | 61 | 64 | 64 | 67 | 67 | 70 | 70 | 73 | 73 | 76 | 76 | 79 | 79 | 82 | 82 | 85 | 85 | 88 | 88
stdu_exp2024
stdu_exp2025_1


Chart: 
| 22 | 22 | 25 | 25 | 28 | 28 | 31 | 31 | 34 | 34 | 37 | 37 | 40 | 40 | 43 | 43 | 46 | 46 | 49 | 49 | 52 | 52 | 55 | 55 | 58 | 58 | 61 | 61 | 64 | 64 | 67 | 67 | 70 | 70 | 73 | 73 | 76 | 76 | 79 | 79 | 82 | 82 | 85 | 85 | 88 | 88
stdv_exp2024
stdv_exp2025_1


5 min data batch
10 min data batch
during analysis
during forecast
The RMS errors of 4DEnSRF are lower than those of EnSRF.
The advantage of 4DEnSRF is more when analysis interval is longer (10 min or longer).
Forecast error with 4DEnSRF grow faster for 10 min data batches than the 5 min case, while the growth rates for EnSRF are fast in both cases.
(Wang et al. 2012 QJRMS)

## Slide 37
KTLX
A tornadic
Supercell
Storm
Wang, Xue and Min (2014 To be submitted)
Analysis of a tornadic supercell on May 10, 2010
EnSRF v.s. 4DEnSRF
dx=1.5 km
dx=0.5 km

## Slide 38
Analyzed T' (shaded), Pressure (contours) and Wind Vectors at 1.5 km AGL
4DEnSRF EnSRF
Much better organization of low-level mesocyclone with 4DEnSRF
Better dynamical consistency between wind, pressure and temperature fields

## Slide 39
Z obs at 23:27Z
Vr obs at 23:27Z
AE5M at 23:26z
OBS
at 0.52°
Elevation
Z, wind, w
analyses
at 1 km
4DEnSRF at 23:26Z
EnSRF at 23:26Z

## Slide 40
Probability of sfc vorticity exceeding a threshold
4DEnSRF
EnSRF

## Slide 41
Probabilities of sfc wind speed exceeding 29 ms-1 (EF0) and 38 ms-1 (EF1)
EF0
EF1
4DEnSRF
EnSRF

## Slide 42
The 10 m maximum wind speed from all ensemble forecasts from 2320 through 2340 for i4DEnSRF and 4DEnSRF, after 10 cycles.
The yellow thick lines mark the reported damage path of tornado J4 in Seminole county.
i4DEnSRF
4DEnSRF
Iterative 4DEnSRF (10 May 2010 case)
(Wang et al. 2014b)
Further Improvement with iEnSRF

## Slide 43
Vision: Warn-on-Forecast
NSSL Warn on Forecast Briefing March 5, 2007
The warning issued based on the computer model forecast(s) includes detailed information on the expected event
Radar and Initial Forecast at 2100 CST
Radar at 2130 CST: Accurate Forecast
Most
Likely
Tornado
Path
T=2120 CST
T=2150
T=2130
T=2140
70%
50%
30%
T=2200 CST
Developing
Thunderstorm
Most
Likely
Tornado
Path
T=2120 CST
T=2150
T=2130
T=2140
T=2200 CST
An ensemble of storm-scale NWP models predict the path of a potentially
tornadic storm. A Warning is Issued!
70%
50%
30%
More than triple current Tornado Warning lead times
Improved warnings allow enhanced community response
(Stensrud, Xue and others 2009)

## Slide 44: 5/20/2013 Moore, Oklahoma Tornado

## Slide 45: Moore, Oklahoma Tornado of May 20, 2013 – 10 km north of Norman
EF5 intensity
Occurred ~3pm
24 people killed
Several thousands of houses destroyed
Warning issued ~15 min before tornado touchdown
Forecast of high tornado potential issued 1 days ahead of time.

## Slide 46
Ensemble Maximum of
Hourly-max Updraft Helicity
Neighborhood Probability of
Hourly-max UH ≥ 50
Probability Matching Mean of Composite Reflectivity
20 hour forecast valid at 20 UTC, 20 May 2013, time of Moore Tornado
by CAPS Storm-Scale Ensemble Forecasting System
Reflectivity from Control Member

## Slide 47: Prediction of Moore Tornadic Storm @5 min intervals @0.5km spacing
t = 10 minutes
(1840 UTC)
Storm initialized
with EnKF
assimilation
of radar etc data
ARPS model
Prediction
dx=500 m

## Slide 48: Prediction of Moore Tornadic Storm @5 min intervals @0.5km spacing
t = 15 minutes
(1845 UTC)
Storm initialized
with EnKF
assimilation
of radar etc data
ARPS model
Prediction
dx=500 m

## Slide 49: Prediction of Moore Tornadic Storm @5 min intervals @0.5km spacing
t = 20 minutes
(1850 UTC)
Storm initialized
with EnKF
assimilation
of radar etc data
ARPS model
Prediction
dx=500 m

## Slide 50: Prediction of Moore Tornadic Storm @5 min intervals @0.5km spacing
t = 25 minutes
(1855 UTC)
Storm initialized
with EnKF
assimilation
of radar etc data
ARPS model
Prediction
dx=500 m

## Slide 51: Prediction of Moore Tornadic Storm @5 min intervals @0.5km spacing
t = 30 minutes
(1900 UTC)

## Slide 52: Prediction of Moore Tornadic Storm @5 min intervals @0.5km spacing
t = 35 minutes
(1905 UTC)
Storm initialized
with EnKF
assimilation
of radar etc data
ARPS model
Prediction
dx=500 m

## Slide 53: Prediction of Moore Tornadic Storm @5 min intervals @0.5km spacing
t = 40 minutes
(1910 UTC)
Storm initialized
with EnKF
assimilation
of radar etc data
ARPS model
Prediction
dx=500 m

## Slide 54: Prediction of Moore Tornadic Storm @5 min intervals @0.5km spacing
t = 45 minutes
(1915 UTC)
Storm initialized
with EnKF
assimilation
of radar etc data
ARPS model
Prediction
dx=500 m

## Slide 55: CAPS’s Multi-scale Parallel EnKF system
Hybrid OpenMP/MPI parallelization
Multiple data types, especially high-density radar data
4D asynchronous filter (4DEnSRF), and iterative procedure (iEnSRF) for faster convergence/spin up
Interface with both ARPS and WRF
Support for 2-moment microphysics, perturbed physics and multi-physics ensemble, build-in attenuation correction
Microphysical parameter estimation
Polarimetric radar data assimilation
Adaptive covariance inflation, successive spatial localization
EnKF-3DVAR hybrid (testing) and LETKF algorithms
En4DVAR (being implemented)
Observation operators build into ARPS (for 4DEnKF).

## Slide 56: Parallel EnSRF algorithm suitable for dense data from large radar networks via domain decomposition Supports hybrid OpenMPI/MPI parallelization
(Wang, Jung, Supinie and Xue 2013 JTech)
Notes: R is maximum localization radius
Grid is decomposed into sub-domains, each domain is assigned to a shared-memory node
Each sub-domain is further divided into S1-S4 sub-patches
Sub-patches with the same label must be at least 2R apart so that obs within them don’t affect common grid points and can be processed simultaneous
Loop through S1-S4 to complete obs assimilation

## Slide 57: Realtime EnKF Radar DA Experiment for CONUS Domain

## Slide 58: First time ever Realtime EnKF Radar DA Experiment for Convective Storms in spring 2013 over ¼ CONUS at dx=4 km 40-member CONUS 6-h ensemble forecasts fed the EnKF analyses for WRF at 00 UTC

## Slide 59: 20 hour forecast using EnKF I.C.
May 20, 2013 Moore Tornado Time

## Slide 60: Reflectivity ETS Scores for 14 forecasts from May-June 2013 (EnKF v.s. 3DVar)
20dBZ threshold
40dBZ threshold
Notes: EnKF cases: 5/19, 5/20, 5/21, 5/22, 5/23, 5/24, 5/27, 5/30, 5/31, 6/3, 6/4, 6/5, 6/6, 6/7
3DVAR cases: 5/20, 5/21, 5/22, 5/23, 5/27, 5/30, 5/31, 6/3, 6/4, 6/5, 6/6, 6/7

## Slide 61
CAPS CONUS Domain 4-km Cycled EnKF DA and Ensemble Forecast Experiment
(Setup for Spring 2014)

## Slide 62: CONUS Domain 4-km Cycled EnKF DA and Ensemble Forecast Experiment (Setup for Spring 2014)
Forecast model: WRF-ARW
Physical domain: CONUS (1200x768x50)
40 member ensemble
DA: 2300, 2315, 2330, 2345, 0000 UTC
Observations: sounding, profiler, surface, radar (Z, Vr)
Microphysics scheme: WSM6 with perturbed N0r, N0g, ρg
Multi-PBL schemes: MYJ, YSU, ACM2, MYNN, QNSE
DA scheme: ARPS parallel EnSRF

## Slide 63
Configurations for 12-member ensemble forecasts
Member | IC | BC | Microphysics | LSM | PBL
enkf_m1 | enk_m1a | arw_cn | Thompson(8) | Noah | MYJ(2)
enkf_m2 | enk_m2a | arw_m3 | MY2(9) | Noah | MYJ(2)
enkf_m3 | enk_m3a | arw_m4 | Morrison(10) | Noah | MYJ(2)
enkf_m6 | enk_m6a | arw_m5 | Thompson(8) | Noah | MYNN(5)
enkf_m7 | enk_m7a | arw_m6 | MY2(9) | Noah | YSU(1)
enkf_m8 | enk_m8a | arw_m7 | Morrison(10) | Noah | YSU(1)
enkf_m9 | enk_m9a | arw_m8 | Thompson(8) | Noah | QNSE(4)
enkf_m10 | enk_m10a | arw_m9 | MY2(9) | Noah | MYNN(5)
enkf_m11 | enk_m11a | arw_m10 | Thompson(8) | Noah | YSU(1)
enkf_m12 | enk_m12a | arw_m11 | WDM6(16) | Noah | YSU(1)
enkf_m15 | enk_m15a | arw_m12 | Morrison(10) | Noah | MYNN(5)
enkf_m16 | enk_m16a | arw_m13 | WDM6(16) | Noah | MYJ(2)

## Slide 64
Spring 2014 15-min Cycled 4-km CONUS Grid EnKF and 3DVAR DA and SSEF
(See Youngsun Jung’s Presentation Thursday)

## Slide 65: 2014 Cycled 4-km EnKF DA
WRF ARW model with multiple physics;
Observations: sounding, profiler, surface, radar (Z, Vr)
Microphysics scheme: WSM6 with perturbed N0r, N0g, ρg
Multi-PBL schemes: MYJ, YSU, ACM2, MYNN, QNSE
DA scheme: ARPS parallel EnSRF
NAM initial background + SREF perturbations
15-min cycles at 2300, 2315, 2330, 2345, 0000 UTC
24-h deterministic and ensemble forecasts
Assimilation of all radar data within CONUS domain: 7 min/cycle!

## Slide 66: 13 April 2014 Squall Line Test
Member | IC | BC | Radar | Micro | LSM | PBL
S4CN | 00Z ARPSa | 00Z NAMf | yes | Thompson | Noah | MYJ
3DVAR | 00Z cycled ARPSa | 00Z NAMf | yes | Thompson | Noah | MYJ
Thom | 00Z EnKFa | 00Z NAMf | yes | Thompson | Noah | MYJ
WSM6 | 00Z EnKFa | 00Z NAMf | yes | WSM6 | Noah | MYJ
3DVAR (Vr)+Cloud Analysis(Z)
EnKF(Vr, Z)
Notes: S4CN is the HWT control member.

## Slide 67
Cycled EnKF
OBS
Cycled 3DVAR/Cloud anx
Non-cycled 3DVAR/cloud anx
Analyzed composite reflectivity (0 hour)
Notes: EnKF and s4cn show good match with observations. Cycled 3DVAR overestimates intensity (maybe some over-adjustment is going on? Need to check). Because of the lack of radar observations over the sea (upper left and lower right corners), spurious echoes were left unsuppressed in 3DVAR experiment. Echoes in the north of the great lakes could be real.

## Slide 68
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
OBS
Non-cycled 3DVAR
Top: EnKF
Bottom: 3DVAR+Cloud analysis
1 hr forecast
Valid at 0100 UTC
13 May 2014
Notes: The shape and location of the rain band in the eastern Texas is better predicted by the EnKF forecast up to 5 hour into the forecast. However, echoes in Wisconsin are too weak and dissipates too early in the EnKF forecast. On the other hand, echoes near the Great Lake are over-predicted in s4cn (HWT control member). The northern part of precipitation system start to weaken at 0600 UTC but dissipation is much delayed in S4CN. Cycled 3DAR show better prediction of the structure and location of the middle part of the line during the medium range (7-16 hr) forecast. From 9 hr forecast, Thom and S4CN forecast become very similar for the southern part of the system (enclosed by pink dashed circles) suggesting the microphysics scheme is taking over the evolution of the system.

## Slide 69
OBS
2 hr forecast
Valid at 0200 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 70
OBS
3 hr forecast
Valid at 0300 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 71
OBS
4 hr forecast
Valid at 0400 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 72
OBS
5 hr forecast
Valid at 0500 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 73
OBS
6 hr forecast
Valid at 0600 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 74
OBS
7 hr forecast
Valid at 0700 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 75
OBS
8 hr forecast
Valid at 0800 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 76
OBS
9 hr forecast
Valid at 0900 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 77
OBS
10 hr forecast
Valid at 1000 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 78
OBS
11 hr forecast
Valid at 1100 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 79
OBS
12 hr forecast
Valid at 1200 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 80
OBS
13 hr forecast
Valid at 1300 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 81
OBS
14 hr forecast
Valid at 1400 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 82
OBS
15 hr forecast
Valid at 1500 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 83
OBS
16 hr forecast
Valid at 1600 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 84
OBS
17 hr forecast
Valid at 1700 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 85
OBS
18 hr forecast
Valid at 1800 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 86
OBS
19 hr forecast
Valid at 1900 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 87
OBS
20 hr forecast
Valid at 2000 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 88
OBS
21 hr forecast
Valid at 2100 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 89
OBS
22 hr forecast
Valid at 2200 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 90
OBS
23 hr forecast
Valid at 2300 UTC
13 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 91
OBS
24 hr forecast
Valid at 0000 UTC
14 May 2014
Top: EnKF
Bottom: 3DVAR+Cloud analysis
EnKF_Thom
EnKF_WSM6
Cycled 3DVAR
Non-cycled 3DVAR

## Slide 92
0.25
0.10
0.01
0.50
Hourly Precipitation ETS Scores
Notes: Cycled 3DVAR forecast show higher ETS score for the surface precipitation than the EnKF Thompson forecast before 6 hr forecast as stratiform rain area and the northern part of system is under-predicted (broken) in the EnKF forecasts.

## Slide 93: A comparison between EnSRF and LETKF algorithms for convective-scale radar data assimilation: OSSEs and Effects of nonlinear observation operator
(Zhao and Xue 2014)

## Slide 94: Outline
Background and motivations;
ARPS-LETKF DA system and OSSE setup;
Comparison of EnSRF and LETKF analyses with radar observations;
Effects of nonlinear reflectivity observation operator;
Summary and conclusions.

## Slide 95: Background
The Ensemble-Square-Root Kalman filter (EnSRF) algorithm (Whitaker and Hamill 2002) (or very similar Ensemble Adjustment Kalman Filter – EAKF) had been used almost exclusively for radar DA at the convective scale;
  A serial algorithm – assimilating one observation at a time
  Easy to implement
  Promising results with radar DA at convective scale
Local Ensemble Transform Kalman Filter (LETKF, Hunt et al. 2007) algorithm is grid-point or state-space based – it updates the state variables using observations within specified influence radii simultaneously.

## Slide 96: Background
The state-space LETKF is easier to parallelize on distributed-memory processors but the algorithm itself is more expensive;
With the observation-space EnSRF algorithm, observations affecting common grid points cannot be analyzed simultaneously - they have to be processed in separate batches (e.g., in parallel algorithm of ARPS EnSRF - Wang et al. 2013);
Because observations are processed independently in EnSRF, localization can be set differently for different observations, offering additional flexibility.

## Slide 97: Background: Previous Studies
Greybush et al. (2011) and Holland and Wang (2013) compared EnSRF and LETKF algorithms using OSSEs
  Both studies used idealized large-scale models with linear observation operators;
  B-localization vs R-localization for covariances;
  Serial vs simultaneous observation processing;
  Some differences were found with the sequential and serial versions of these algorithms, and with B versus R-based localization;
  R-localization and simultaneous processing tend to produce more balanced analyses although differences tend to be relatively small.

## Slide 98: LETKF Algorithm and Implementation
LETKF has been applied successfully to global, regional, and mesoscale NWP models (Szunyogh et al. 2008; Seko et al. 2011; Miyoshi and Kunii 2012);
LETKF has not been applied to the radar DA problem until very recently;
We implemented LETKF within the ARPS ensemble DA framework (Tong and Xue 2005; Xue et al 2006) and compare LETKF and EnSRF in OSSEs for a supercell storm

## Slide 99: Localization Schemes in Ensemble Filters
To suppress the impact of observations from distant regions upon an analysis caused by spurious correlation in due to sampling error
B-localization applied to Kalman gain K, in EnSRF
R-localization applied to Kalman gain K, in LETKF
Regulated R-localization (Nerger and Janjic 2012)
is the localization weight function, which is distance-dependent function. In this work, it is 5th-order correlation function introduced in Gaspari and Cohn (1999)
Notes: To suppress the impact of observations from distant regions upon an analysis caused by spurious correlation due to sampling error
Also increase the rank
First step is to select the observations only from a region surrounding the location of the analysis grid. Actually this step is intrinsically contained in LETKF at the step 3 of LETKF algorithm. The data selection method is used in Houtekamer and Mitchell (1998). LEKF and LETKF are named with “Local” just for this local analysis approach. In addition to providing better results, this localization approach allows the LETKF analysis to be done more efficiently as a parallel computation (Hunt, Kostelich et al. (2007)). However, in this way, the weighting function of the localization is the Heaviside function that weights 1 inside and 0 outside the domain (Miyoshi and Yamane (2007)), then abrupt localization cutoff can result in a noisy analysis (Greybush, Kalnay et al. (2011)). So Hunt et al. (2007) proposed a “smoothed localization”, called R localization, also called “observation localization” in Nerger and Janjic (2012), by multiplying the observational error variance (which is the element of diagonal matrix R) by the inverse of a localization weighting function. This weight function, also called localization function, decays smoothly from one to zero as the distance of the observations from the analysis grid point increases.

## Slide 100: Radar Data OSSEs with a Supercell Storm
20 May 1977 in Del City supercell storm simulation using ARPS model (Tong and Xue 2005);
Model variables:
Lin ice microphysics and 1.5-order TKE SGS turbulence;
64 × 64 × 16 km3 domain, dx=dy=2km, dz=500m;
Del City sounding, storm triggered by a thermal bubble;
Vr and Z data simulated on 14 elevation levels of a single S-band 88D radar;
40 members; 12% inflation, ~6 km localization radius by EnSRF
DA every 5 min from 25 min through 100 min
0
20min
(ensemble initialization)
25min(1st anx)
anx cycle
ending time
60min(8th anx)
100min(16th anx)
Truth simulation
start time

## Slide 101: Simulation of Radar Data
Observation operators
is linear without considering the effect of hydrometeor sedimentation, Z has strong nonlinearity.

## Slide 102: LETKF and EnSRF Experiments
1st determine optimal localization radii for EnSRF and LETKF
Inter-compare LETKF and EnSRF analyses and forecast errors in DA window
  Both Vr and Z
  Only Vr
  Only Z
  Only Z but thinned or in separate batches

## Slide 103: RMSEs of LETKF and EnSRF with Vr+Z Data
Optimal radius for R-localization (3500m) is shorter than B-localization (6000m); But regulated R-localization has a similar optimal localization radius of 6000 m
In the initial spin-up stage, EnSRF outperforms LETKF
LETKF and EnSRF perform similarly after the initial spin-up period
U V W PT P
qc qr qv, qi qs qh

## Slide 104
t=25min
wind field and radar reflectivity in X-Z cross-section
Truth
EnSRF
LETKF
After first analysis, EnSRF analysis is closer to truth.
Wind Reflectivity

## Slide 105: EnSRF vs. LETKF with Vr data only
Similar performances in final stable stages
LETKF is slightly better than EnSRF in the early stage
Simultaneous LETKF analysis might have helped to produce more balanced analyses
U V W PT P
qc qr qv, qi qs qh

## Slide 106: EnSRF vs. LETKF with Z data only
Similar performances in final stable stages
In spin-up stage, EnSRF outperforms LETKF at analysis step (esp. for the Z-related variables, qr, qs and qh);
U V W PT P
qc qr qv, qi qs qh

## Slide 107: RMS Difference to radar observation: EnSRF vs. LETKF with only Z used
Similar performances in final stable stages
In spin-up stage, EnSRF outperforms LETKF at analysis step obviously, esp. for Z reflectivity;
At forecast step, RMSD of EnSRF jumps back at forecast step;

## Slide 108: Effects of Nonlinear Observation Operator
Implicit linearization of nonlinear operator in EnKF
(1)
(2)
(3)
The linearization is implicit in Eqs. (1) ~(2) although full nonlinear operators are used (Lorenc 2003);
This implicit linearization is around ensemble mean state of possibly different quality, from different stages of the analysis cycle.

## Slide 109: Effects of Nonlinear Z Observation Operator
In EnSRF, effective linearization of Z operator for subsequent observation is made around the newly updated, intermediate ensemble during the serial processing;
Updated ensemble is better than the prior ensemble, especially during the early cycles when ensemble state is poor;
The improved intermediate ensemble helps EnSRF outperform LETKF;
Differences become small when state estimation becomes good – when analysis increments are small.
Notes:   Why Different linearization leads to different analysis, and linearization about better state helps EnSRF outperform LETKF

## Slide 110: Effects of Nonlinear Observation Operator
In LETKF, linearization is made about the entire prior ensemble since all the observations are processed simultaneously;
In EnSRF, linearization for subsequent observation is made around the newly updated, intermediate ensemble during the serial processing;
Updated ensemble is better than the prior ensemble, especially during the early cycles when ensemble state is poor;
The improved intermediate ensemble helps EnSRF outperform LETKF (our hypothesis);
Differences become small when state estimation becomes good – when analysis increments are small.
Notes:   Why Different linearization leads to different analysis, and linearization about better state helps EnSRF outperform LETKF

## Slide 111: Experiments to Test the Hypothesis
Experiments are designed to deliberately remove the differences of linearization or sequential v.s. simultaneous processing of EnSRF and LETKF
  Experiment 1: Thinned Z data
  Experiment 2: LETKF analysis with 2 batches of Z observations

## Slide 112: Experiment 1: Thinned Z Observations
Z observations are thinned (red dots) to have spacing larger than cut-off radius in horizontal;
Observations analyzed earlier have no influence on the state used by later observation operators hence not affecting linearization in EnSRF;

## Slide 113: EnSRF vs LETKF with Thinned Z Observations
Differences between ENSRF and LETKF are mostly gone in early cycles
Notes: In the final stage,
  some difference in the RMSD of wind components, which might be related to the effect of localization on balance; less imbalance in LETKF analysis
  for difference in the RMSD of reflectivity, it is because the observations are only thinned in horizontal, so there is still effect of nonlinear observation through vertical direction.

## Slide 114: Exp. 2: LETKF analysis with 2 batches of Z observations
Z observations are split into 2 batches:
  batch 1 includes thinned data used in Exp.1;
  batch 2 includes the remaining data;
LETKF effectively runs in a partially sequential processing mode;
By providing better prior ensemble for the 2nd batch LETKF analysis, effects of linearization are reduced.

## Slide 115
LETKF with 2 Batches of Z Observations
LETKF with 2 batches is much closer to EnSRF than LETKF with 1 batch.
Can be seen more clearly from RMSD of Vr and Z (not shown)
2 batches
Notes:   the original reflectivity dataset is split into 2 smaller datasets. Then LETKF processes the 2 smaller datasets in 2 analysis batches sequentially. In each analysis batch, the observations in the smaller dataset are still processed simultaneously.
black curve is for EnSRF;
red curve is for LETKF with all the observation in 1 batch;
blue curve is for LETKF with 2 batches of observation.

## Slide 116: Summary and Conclusions
LETKF can effectively assimilate radar observations and produce similar analyses as EnSRF after a few DA cycles.
The optimal cut-off radius for R-localization in LETKF is shorter, but that for regulated R-localization is similar to that of B-localization in EnSRF;
Simultaneous processing in LETKF appears to produce slightly more balanced analyses than serial EnSRF when assimilating linear Vr data;
EnSRF outperforms LETKF noticeably when assimilating nonlinear Z data during the initial cycles when state estimation is poor;
The differences are demonstrated to be due to different degrees of effective linearization of the nonlinear Z operator, essentially due to sequential v.s. serial data processing.

## Slide 117: EnKF for Storm-Scale DA - Summary
Capable of dealing with complex ice and multi-moment microphysics, which reduce model error;
Effective in assimilating reflectivity data;
Can assimilate polarimetric radar data directly;
Can assimilate attenuated reflectivity directly (not shown)
Does not require adjoint model;
Algorithm more parallelization-friendly than 4DVAR;
Can produce much more balanced analyses than 3DVar;
Can update and provide ensemble perturbations for EnVar hybrid;
4DEnKF outperforms 3DEnKF;
iEnKF helps during initial cycles;
EnKF and LETKF very similar, more difference found with NL obs operator;
Can retrieve MP DSD parameters;
We are at the stage of performing realtime testing.

## Slide 118: Important Questions
3D/4DEnVar v.s. 3D/4DEnKF
  Any value of static B at all at convective scale?
  Equation constraint and state space localization?
  Multi-scale issue? How to deal with localization for very different spatial characteristics (radar/satellite versus rawinsondes)?
  Spatially adaptive localization (convective v.s. clear air regions)?
  Adjoint-based 4DVar difficult – how to properly localize for fast moving storms in 4DEnVar/4DEnKF when flow-following localization is important?
  Running-in-Place/iterative EnKF – how useful and when to use?
  EnSRF v.s. LETKF?
  How to deal with large model errors?
At CAPS, a hybrid 4DEnKF/4DEnVar systems has been developed base on ARPS 3DVAR and ARPS EnKF in a consistent framework, allowing us to answer some of these questions through carefully designed experiments.

## Slide 119: 4DEnKF-En4DVar Hybrid
Obs
t0
Obs
Obs
Obs
Obs
Obs
Obs
t1
4DEnKF
4D Assimilation Window – 1 cycle
En4DVar
Obs
Obs
Notes: The EnKF is a 4-d data-assimilation method that uses a Monte-Carlo
ensemble of short-range forecasts to estimate the covariances of the forecast
error (Evensen,1994).

## Slide 120: 4DEnKF-En4DVar Hybrid
Liu, C., and M. Xue, 2014: A unified framework for four-dimensional ensemble-variational hybrid data assimilation. Quart. J. Roy. Met. Soc. Submitted
Combine benefits of 4DVAR and EnKF
  Can assimilate high-frequency data in 4D windows
  Carry ensemble covariance through assimilation cycles
  Does not require tangent linear or adjoint model
En4DVar-NPC-FGAT:
Static covariance
Ensemble covariance

## Slide 121: Development of a Coupled EnKF-En3DVar/En4DVar Hybrid DA System suitable for Radar DA
Integrated recent, new developments into an updated 3DVAR package
    To be able to analyze reflectivity directly for mixed phase microphysics;
    Diagnostic pressure equation constraint;
    Radar data on elevation levels and using of beam pattern weighting (as in EnKF)
Developed a unified theoretical framework for En3DVar/En4DVar ;
    Efficient 4DEnVar formulation without requiring adjoint
Implemented 3DEnVar and 4DEnVar, coupling it with CAPS EnKF;
    Testing it with OSSE radar data;
    To compare with 3DVar, 3DEnSRF, 4DEnSRF, 3DLETKF, 4DLETKF
To directly support WRF model also;

## Slide 122: Development and Testing of GSI-Based EnKF and EnKF/3DVAR Hybrid Data Assimilation Systems for the Operational Rapid Refresh System
Zhu, K., Y. Pan, M. Xue, X. Wang, J. S. Whitaker, S. G. Benjamin, S. S. Weygandt, and M. Hu, 2013: A regional GSI-based EnKF system for the Rapid Refresh configuration: Results with a single, reduced resolution. Mon. Wea. Rev., 141, 4118-4139.
Pan, Y., K. Zhu, M. Xue, X. Wang, M. Hu, S. G. Benjamin, S. S. Weygandt, and J. S. Whitaker, 2014: A regional GSI-based EnKF-variational hybrid data assimilation system for the Rapid Refresh configuration: Results with a single, reduced resolution. Mon. Wea. Rev., 142, 3756-3780.
(Zhu et al. MWR 2013; Pan et al. MWR 2014)
(Supported by FAA Aviation Weather Research Program
- Very limited funding)

## Slide 123: Ensemble and Ensemble-Variational DA
The benefit of flow-dependent B for DA is well recognized.
Ensemble-derived B can be used directly in EnKF or via variational formulations, either alone or in combination with static B (with hybrid B)
Hybrid En3DVar coupled with EnKF has been implemented at NCEP for the global GFS since 2012.
NCEP regional models (NAM, RR and HRRR) still use GSI 3DVAR.
This talk reports on the development and testing of regional EnKF and EnKF/En3DVAR hybrid for the Rapid Refresh (RR) system.
Both regional and global hybrid DA share the same framework and code base, and are based on the operational GSI 3DVAR.

## Slide 124: First, EnKF and GSI Results at Reduced 40 km Resolution
40 km reduced resolution grid (for lower costs)
40 ensemble members, adaptive inflation
Nine-day-long period with 3-hourly assimilation cycles during spring 2010
All data used by operational RR system, initially without satellite data
Single set of physics v.s. multiple-physics ensemble
Best results obtained with observation-type and height-dependent localization radii
Comparison with similarly configured GSI

## Slide 125
Rapid Refresh（RR）System
~13km, hourly DA cycles, WRF-ARW dynamic core, currently using GSI 3DVAR
Developed at GSD/ESRL and run operationally at NCEP
Replaced original RUC (Rapid Update Cycles) in 2012
RR
RUC

## Slide 126
Observation Distribution Valid at 2010051412
PROFLR
ADPUPA
VADWND
ADPSFC
ADPSFC
SFCSHP
AIRCAR
ADPSFC
SATWND
SATWND
AIRCFT
AIRCFT

## Slide 127: EnKF v.s. GSI
Zhu et al. (2013 MWR)

## Slide 128
Horizontal distribution of selected observation kinds
Sounding and profiler
Surface data from land stations and ships
Aircraft
Satellite retrieval winds
GPS PW and Sat
radiance data
not included

## Slide 129
List of EnKF Experiments
Inflation

## Slide 130
Physics options used
in multi-physics
Ensemble
(radiation, sfc layer,
PBL and cumulus)

## Slide 131
RH
T
U
V
Average Fcst RMSEs
Verification against upper air soundings – Forecast RMSES
Notes: The first row is the 3 hour forecast RMSE in the vertical distribution. The second is the domain and time averaged RMSE (3 to 18 hours).

## Slide 132
Surface variable forecast verification - against surface stations
Surface pressure
2m RH
2m T
10m U
10m V
When multiple-physics is employed, EnKF consistently outperforms GSI in surface variable verification
Height-dependent localization radii are used.
Notes: Slide 5-7 is for the outer domain forecast (40km horizontal resolution)

## Slide 133
3h forecast RMSE profiles against soundings
RH
RH
T
Temperature
U
V
GSI errors
larger at
all levels
Multi-physics
Improves
results
Notes: The first row is the 3 hour forecast RMSE in the vertical distribution. The second is the domain and time averaged RMSE (3 to 18 hours).

## Slide 134
A
A
A
Stage IV hourly
precipitation
EnKF 13km 11 h forecast
from 2010051012
GFS 13km 11 h forecast
from 2010051012
Notes: Slide 8-11 is for the inner domain precipitation forecast (13 km horizontal resolution)
The first case is the May 10th OK tornado outbreak. The first row is 9 hours forecast start from 12 UTC May 10 2010; The second row is 11 hours forecast. Since the model resolution is of 13km, we didn’t expect the forecast to describe the detail of storm structure. For both EnKF and GSI, the predicted storms are relatively weaker than observation. But EnKF is better than GSI in the prediction of storm position and intensity. It could be seen the EnKF predicted rainband is very close to the observation with several scatted storms along the dry line. Moreover, it describes largest storm A which suited in the south boundary of Kansas pretty well. However, the GSI predicted rainband is moving slowly and about half degree west to the observation. It almost failed to describe the storms within the Oklahoma state.

## Slide 135
EnKF is consistently better than GSI for the precipitation forecasts
Positive impacts of AMSU and AIRS radiance data also obtained with EnKF better performing than GSI (not shown)
13-km hourly Precipitation Forecast ETS Scores from EnKF_Multi5 and GSI_Ctr
Notes: The time averaged GSS scores of above slide. It could be seen that EnKF consistently outperforms GSI. As a further examination, we also calculated GSS scores using higher threshold: 1.25mm/h and 2.5 mm/h. The conclusion is the same as the smaller threshold that EnKF is consistently better than GSI. In all, the verification scores indicate the EnKF improve the precipitation forecast.

## Slide 136: En3DVAR Hybrid v.s. EnKF and GSI 40km Single-Resolution Results
Pan et al. (2014 MWR)

## Slide 137: Ensemble-Variational (EnVar) Hybrid DA
Use of ensemble-derived B in variational DA framework
  Allows flow-dependent B
  Take advantage of existing variational DA infrastructures
  More robust for small ensembles
  Allows inclusion of equation constraints
  Allows model space localization – needed for non-local observations (radiance, GPS RC, etc)
  Allows for 4DVAR hybrid
EnVar systems still requires the update of ensemble perturbations (using EnKF or ensemble of Var)

## Slide 138
Extended alpha control variable method (Lorenc 2003)
Extra term associated with extended control variable
Extra increment associated with ensemble
GSI-Hybrid: Method

## Slide 139
Two-way feedback
EnKF
En3DVAR
Flowchart of Coupled EnKF-En3DVar Hybrid System

## Slide 140
Localization and Inflation Configurations
Experiments | Horizontal localization (KM) | Vertical localization ( ln(p) ) | Fix inflation | Adaptive inflation
EnKF | 1000 (height-dependent) | 1.1/1.6 (height- and observation-type- dependent) | 0.1 | 0.9
Hybrid1W_Ctl/ Hybrid2W_Ctl | ~1000 (constant) | ~1.1 (constant) | / | /
Hybrid_HD | The same localization used for EnKF | The same as localization for U&V used in EnKF | / | /
Localization radii for EnKF
RH & T
U&V
Horizontal radius vertical radii
Notes: The cut-off radii used in the well-tuned EnSRF control experiment of Z13 (EnKF_CtrHDL in their paper) are height- and observation-type dependent based on the vertical position of the observations. The horizontal cut-off radius at the model top is 1.5 times the value at the surface for all state variables; as shown in Fig. 3a, increases from 700 km at the surface to 1050 km at the model top. The vertical cut-off radius is not only height dependent, but also observation-type dependent. For RH and T observations (solid line in Fig. 3b), the vertical cut-off radii at the model top and surface are set to a quarter of 1.1 and half of 1.1, respectively. For wind observations (dash line in Fig. 3b), is twice as large as that for RH and T observations. For surface pressure observations and GPS PW data (which are most strongly linked to low-level moisture), their vertical localization radii are set to a constant value of 1.6. These settings were used in the control experiment of Z13, and their choices were guided by the correlation scales found in the NMC-method-derived error statistics used by GSI 3DVar and were further tuned based on sensitivity experiments.

## Slide 141
3-18 h forecast RMSEs against soundings
RH
T
U
V
Hybrid 2way
Hybrid 1way
GSI 3dvar
EnKF
In 3D RMSES, hybrid better than EnKF in T, U, V fcst, slightly worse for RH
Now includes
GPS PW data

## Slide 142
EnKF:
Horizontal localization: 1000km
Vertical localization: 1.1 (lnp)
Fix Inflation: 0.1
Adaptive Inflation: 0.9
Hybrid:
Horizontal localization:1000km
Vertical localization: 1.1 (lnp)
Weight of static covariance: 0.5
Hybrid 2way
Hybrid 1way
GSI 3dvar
EnKF
Hybrid
improves Psfc, RH
degrades T, U, V
3-18 hour Surface variable forecast verifications
Psfc
RH
T
U
V
18h
3h
EnKF better here

## Slide 143
Hybrid 2way
Hybrid 1way
GSI 3dvar
EnKF
Verification of 3-h forecasts against soundings
3 h fcsts
3 h fcsts
3h RH
T
U
V
Obs-type dependent
Localization in EnKF
Key for the difference
3h fcst
RMSE
Profiles

## Slide 144
3-h forecast RMSEs verified against soundings through cycles
08/12
16/00 (day/hour)
12/12
RH
T
U
V
GSI
GSI
GSI
GSI
8 days
Notes: After May 10th, the differences among experiments turns stable indicates the ensemble has been spined up

## Slide 145
GSS/ETS scores for Precipitation Forecasts on 13 km Grid
Positive Impact of Hybrid somewhat less than Pure EnKF

## Slide 146
EnKF
En3DVAR
Dual-Resolution RR Hybrid System
40 km
13 km

## Slide 147
Sensitivity Experiments | Weight to ensemble covariance
GSI13C | 0.0
HybridD05 | 0.5
HybridD09 | 0.9
HybirdD10 | 1.0
Hybrid1W13 | /
Hybrid1W13 is the 13 km forecasts launched from the interpolated fields from 40 km Hybrid1W_Ctl analyses.
GSI13C is the pure 13 km GSI 3DVAR experiment
Dual-resolution improves precipitation skills for long time forecast at low threshold, and high thresholds.
Different from single-resolution 40 km hybrid experiments, dual-resolution using full ensemble covariance slightly outperforms those using half ensemble covariance.
HR-GSI
HR GSI
HR-GSI
DR-hybrid
LR-hybrid
Precipitation ETS Scores
>0.1mm/h
>1.25mm/h
>2.5mm/h
DR-hybrid
LR = 40 km
HR = 13 km

## Slide 148
Dual-resolution improves precipitation skills for long time forecast at low threshold, and high thresholds.
Different from 40 km hybrid experiments, dual-resolution using full ensemble covariance slightly outperforms those using half ensemble covariance.
HR-GSI
HR GSI
HR-GSI
DR-hybrid
LR-hybrid
Hourly Precipitation Forecast ETS Scores
>0.1mm/h
>1.25mm/h
>2.5mm/h
DR-hybrid
LR = 40 km
HR = 13 km

## Slide 149: Summary
The GSI-based EnKF, and EnKF-En3DVAR hybrid DA systems are established for the Rapid Refresh system
EnKF running at reduced 40-km resolution out-performs similarly configured GSI for both conventional state variables and for precipitation forecasts produced on 13 km grid.
The use of multiple physics further improves the EnKF results, especially at the lower levels.
The use of height- and observation-type-dependent localization radii improves EnKF results.
Coupled with single-physics EnKF, the single-resolution hybrid further improves the pure EnKF for conventional variable, but not for precipitation.
High-resolution analyses on the 13 km grid, either with dual-resolution hybrid, or 13-km GSI, improve precipitation forecasts, but do not necessarily improve sounding verification.

## Slide 150: Future Work with Regional GSI System
Test and operationalize regional EnKF and EnVar hybrid for RR (and possibly NAM – collaborative effort with ESRL and EMC)
Establish and test 13/3km configurations for HRRR.
Adding radar reflectivity and radial velocity assimilation capabilities into GSI-ARW system (coding mostly completed), initially using CAPS’s parallel EnKF as the second step to GSI-based EnKF for handling radar data.
Reflectivity observation operators consistent with model microphysics (Thompson for RR and HRRR).
Lots of tuning and testing.
A proposal submitted to Round 1 of Research to Operation Initiative to accelerate this effort (as well as to provided needed support for Storm Scale Ensemble Prediction efforts to HWT)