## Slide 1
N
Evaluation of Potential NMMB CMAQ Configurations for the July 2011 Operational NAQFC Implementation
February 17, 2011

## Slide 2: Implementation Options with NMMB Coupling
CMAQ with CB05 upgrades
  Combo: bundled upgraded CB05 run
    M-O similarity theory deposition velocity (exp1)
    Improved canopy resistance (exp2)
    Minimum PBL height (exp3)
    GEOS-5 Chem dynamic LBCs (exp4)
  Combo1 : combo + satellite derived canopy heights
    Other (biogenics, additional deposition velocity changes…)
NMMB CB-IV Default
  Gas phase Carbon Bond IV mechanism only
    PM Predictions not available
    Reduced Volatile Organic Compounds (VOC) speciation
  -Using CB-IV based 2005 Emissions Inventory
Delay NMMB implementation

## Slide 3
CMAQ CONUS Domain Tests for
Summer 2010
Simulation | CMAQ physics | CMAQ chem | Vertical Coupling | CMAQ mapping to USGS
NAM PROD | Default | CB-IV | Unified | USGS
NAM EXP | Default | CB05, AERO-IV | Unified | USGS
NAM combo1 | Vd PBLH LBCs | CB05, AERO-IV | Unified | USGS
NMMB combo1 | Vd PBLH LBCs | CB05, AERO-IV | Interpolated | From USGS
NMMB prod | Default | CB-IV | Interpolated | From USGS

## Slide 4
NCEP Air Quality Forecast 2010 Verification
Daily 8h Max O3 Threshold performance
NAM-Production(CB04) vs NCO-Para (CB05), East vs West
NCO/PARA CB05 run ETS is Improved over Western U.S .
BUT Skill reduced over East
CSI
Bias
Equitable Threat Score
Fraction Correct

## Slide 5
NCEP Air Quality Forecast
NAM-CMAQ OPS vs EXP
(8 hr Max Ozone East vs West U.S. for Day 2)
Current Exp/Para system (dashed line):
Increasing error as Summer progressed for Eastern U.S.
2010 RMSE
Aug. 1
2010 BIAS
Aug. 1

## Slide 6: Operational vs Experimental Verification Day 2 Ozone 8h daily maximum August 10, 2010
Strong overprediction esp. along Long Island Sound and DC metro area

## Slide 7
NCEP Air Quality NAM-Combo1 Experiments
(Daily 8 hr Max ozone CONUS Errors for Day 2)
NAM –CB05- Combination1 run (dashed red) improved
compared to Experimental/Para CB05 (dashed black)
BUT combo1 run RMSE are still worse than NAM-CBIV Prod(solid black)
BIAS
RMSE
Para/Ctl
Prod
NAM-CB-IV PROD
NAM-CB05 EXP/PARA
NAM-CB05 Control (same config as EXP/PARA)
NAM-CB05 Combo1

## Slide 8: NEMS-NMMB Coupling Tasks
Vertical coupling: NMMB hybrid with CMAQ sigma
  Tight (ARL)
  Equivalent sigma (ARL)
  Interpolated (Marina, Youhua)
MAP NEMS-NMMB IGBP land-use characteristics to CMAQ USGS
Land use categories.
Impacts:
  Biogenic emissions
  Chemical deposition processes
Couple NMMB with Production CMAQ CB-IV Configuration
August 2010 retrospective NMMB-CMAQ runs
Real-time NAM-B CMAQ EMC parallel runs

## Slide 9
1. Loose coupling: equivalent sigma - Temperature
High terrain

## Slide 10
2. NMMB new IGBP Land Use
11: Deciduous Broadleaf Forest
15: Mixed Forest

## Slide 11
Black: NAM-CMAQ CB IV
Red: NMMB-CMAQ CB IV
Dashed: NMMB-CMAQ CB05 combo1
CMAQ driven by NAM vs NMMB
Daily 8h-max O3 error by Threshold (ppb)
NMMB-CBIV system similar to NAM-CBIV Operational
NMMB-CBIV bias improved for >65 thru >85 thresholds

## Slide 12
Black: NAM-CMAQ CB IV
Red: NMMB-CMAQ CB IV
Dashed: NMMB-CMAQ CB05 combo1
Daily RMSE & BIas CONUS 8h-max O3
NMMB-CBIV system RMSE similar to NAM-Production
NMMB-CBIV bias worse esp. August 20-24th

## Slide 13
Black: NAM-CMAQ CB IV
Red: NMMB-CMAQ CB IV
Dashed: NMMB-CMAQ CB05 combo1
Daily RMSE & Sub-regions 8h-max O3
Northeast RMSE
Southwest RMSE
NMMB-CBIV worse than Production over North East
NMMB-CBIV & CB05 better than Production over South West

## Slide 14
Black: NAM-CMAQ CB IV
Red: NMMB-CMAQ CB IV
Dashed: NMMB-CMAQ CB05 combo1
Diurnal Cycle RMSE East vs West 1h-avg O3
Early morning error spike for only NMMB runs in East
  Higher NMMB-CMAQ PBLH contributes to residual layer mixing
Early morning error spike for all runs in West

## Slide 15: Summary
CMAQ CB05 Configuration Experiments
Combo1 configuration performs best
  Further calibrations needed with NMMB (e.g: deposition velocity)
Changes are appropriate only for CB05 chemistry
NMMB Coupling
In general CB-IV configuration
  performs best for threshold daily max statistics except over Southwest
  RMSE are improved over East but worse over West
Early morning error spike more evident for NMMB runs in East
  Deeper PBLH in NMMB mixes down residual pollutant airmass
Questions
Impact of higher Initial conditions with CB05 runs
CB05 performance degradation primarily in rural areas or lower ozone events
Impact of potential NMMB radiation change

## Slide 16: FY11 NAQFC Plans (besides maintenance, verification, etc)
Para/Prod Upgrades
July 2011: PROD: NMMB-CMAQ loose vertical coupling + 2011EI
Aug 2011: PARA: NMMB CMAQ V4.7.1, tight vertical coupling
Oct 2011: Global Para: NEMS-GOCART In-line (Sarah Lu)
Developmental Testing (PM Improvements)
CMAQ V4.7.1
  w/ Smoke & dust sources
  On consistent NMMB grid (rotated lat-lon, RLL)
  PBL mixing w/ NMMB eddy diffusivity
GSI AIRNOW PM2.5 Data Assimilation
Test optimized CMAQ system
DT&E 4 km NMMB met and CMAQ

## Slide 17: ARL Progress/Plans