## Slide 1: An Overview of Observational Data Processing at NCEP (with information on BUFR Format including “PrepBUFR” files)
Dennis Keyser
NWS/NCEP/EMC
dennis.keyser@noaa.gov
GSI Tutorial
August 6, 2013

## Slide 2
TOPICS COVERED:
Obs processing/dataflow at NCEP
How BUFR fits into the “big picture”
Interacting with BUFR files via NCEP BUFRLIB software
  BUFR Tables
  Reading
  Writing
  Appending observations
Where to go for help
WHAT’S NOT COVERED:
Details on how to read and write all types of BUFR data

## Slide 3: Overview of observational processing and dataflow at NCEP
Managed jointly by NCEP Central Operations (NCO) and NCEP/EMC
Almost all observational data at NCEP eventually ends up in BUFR format (Binary Universal Form for the Representation of meteorological data)
  Relies on NCEP BUFRLIB software (more about that later)
Four stages:
  Data flow into NCEP
  Continuous decoding of data and accumulation into BUFR database or “tank” files (large files holding 24 hrs of data)
  Network-specific generation of dump files (1 to 6 hr time-windowed, duplicate-checked BUFR data read from tanks)
  Generation of PrepBUFR files (QC’d “conventional” obs from dump files, read by GSI)

## Slide 4
GTS
NWSTG/TOC
“Gateway”
NESDIS
GSD
Radar
ROC
LDM
BUFR
Tanks
/dcom
Satellite ingest
(decode)
WGET/LFTP
LDM
tranjb
ECFLOW job queries NESDIS servers for new data
Inside NCEP
Outside NCEP
TNC
Conventional data
GSI
Analysis
Non-conventional Data
Global Guess (perhaps relocated)
Observation error
BUFR mnemonic table
Parm cards
tcvitals
tranjb
Code developed by NCO
Code developed by EMC
PrepBUFR
File
dumpjb
Dump
Files
/com
PrepBUFR
Processing
Modules:
PREPRO
PREVENT
VIRTMP
SYNDATA
CQCHT
RADCOR
CQCPROF
CQCVAD
NRLACQC
OIQC
Post-GSI
PrepBUFR
File
(future)
tranjb
Code
developed
by
NCO & EMC
Gather
Data
(PMB)
Decode
Data
(SIB)
tranjb

## Slide 5
GTS = Global Telecommunications System
  World wide data gathers in GTS
  Sends data to NWSTG/TOC or the “Gateway”
NWSTG/TOC = NWS Telecommunication Gateway/Telecommunication Operations
Center
  Intercepts GTS messages
  Sends data to NCO via TNC (TOC to NCEP Communications) line and via LDM (Local Data Manager)
GSD = NOAA/ESRL/GSD
  Provide Mesonet data to NCO via LDM several times hourly
  SIB converts data from NetCDF to WMO BUFR
Radar/ROC = NOAA Radar Operations Center
  For more information on how Radar data is processed see
  http://www.emc.ncep.noaa.gov/mmb/data_processing/data_processing/
NESDIS = National Environmental Satellite, Data, and Information Service
  Servers:
    DDS – serves up POES data
    SATEPSDIST1E – serves up GOES data
  EMC runs ECFLOW jobs to query the NESDIS servers for new data

## Slide 6
NCO = NCEP Central Operations
PMB = NCO/Production Management Branch, two groups with EMC interaction:
  Data Flow - pull data from the outside
    Interacts w/ the “Gateway”, LDM, ROC, etc. …
    Data retrieval occurs continuously
    Gather all the data then pass it off to SIB for decoding
  SPA group – make sure production is running 24x7 & implement change
SIB = NCO/Systems Integration Branch, one group with EMC interaction:
  Decoders - translate data from their native format to NCEP BUFR, includes:
ACARS (MCDRS), Aircraft (AIREP, PIREP, AMDAR, TAMDAR, RECCO), Land Sfc (SYNOP,
METAR), RADAR (VAD winds, WSR-88D, Canadian, P3 TDR), Oceanographic (Bathy, TESAC,
TRAKOB), Marine Sfc (Ship, Buoy, Tide Gauge, Coast Guard, CMAN), RARS, Profiler/RASS
(NPN, MAP, Europe, Japan, Hong Kong), Upper Air (RAOB, PIBAL, DROP), GPS-IPW,
GPS-RO, USGS River/Stream, SHEF (precip, land & marine sfc), Satellite Wind (JMA,
EUMETSAT, India), CREX (marine sfc), Satellite Altimetry/Wave, Mesonet (incl. COOP, CRN,
HYDRO, SNOW), SEVIRI, Lightning, LaRC Cloud, AIRNOW (ozone)
  Decoding operates continuously on both WCOSS machines (prod & dev)
  NCEP BUFR files stored in the database “tanks” on the WCOSS machines
  “tranjb” is the process that takes a single BUFR file and appends it to the appropriate database tank

## Slide 7
EMC = Environmental Modeling Center
  Runs ECFLOW jobs periodically to query NESDIS servers for new data files
    Compares list of files on server against local history file
  Retrieves new data via WGET or LFTP file transfer protocol
  Converts native data to NCEP BUFR and stores them in the database tanks
  “tranjb” is the process that takes a single BUFR file and appends it to the appropriate database tank
  Processing runs on both NCEP WCOSS machines (prod and dev) at
  discrete wall-clock times defined for each data type
  Satellite data types decoded here include:
    1B radiances from GOES (sounder and imager), SSM/IS, ATOVS (AMSU-A, AMSU-B, MHS,
    HIRS-3, HIRS-4), AQUA/TERRA (AIRS, AMSU-A, IASI), AVHRR/GAC, NPP (ATMS & CrIS)
    Cloud data from GOES (via NESDIS & LaRC), global cloud analyses from AFWA & CLAVR
    Temperature soundings from ATOVS
    Sat-derived winds from GOES (IR, WV-img, WV-snd, VIZ), MODIS (IR, WV-img), AVHRR (IR)
    Scatterometer winds from ASCAT, WindSat
    Rainfall from TRMM/TMI
    SST from POES (via NAVO & NESDIS), GOES, global SST analyses
    Ozone from SBUV-2, GOME-2, OMI, MLS
    Aerosol, Green Vegetation Fraction and smoke from NESDIS (Global)
    Daily snow and ice analyses from NESDIS & USAF
    Imager data (11 µ channel) from GOES

## Slide 8: Database “Tanks”
BUFR
Arranged by UTC day and continuously grow throughout the day
No QC (other than rudimentary checks inside decoders)
No duplicate checking
On WCOSS in /dcom/us007003/yyyymmdd/bmmm/xxsss
  (where mmm is WMO BUFR message type and xxx is local BUFR message subtype)

## Slide 9: Dump Files
BUFR
Generated on production WCOSS machine from “tanks” at each network data cutoff time
Time-windowed, geographically filtered (if RGL)
Duplicate checked
QC: NCEP/SDM purge (or keep) flags, reject list flags, and OPC marine flags on data
Post-dump processing lists dump contents of files, sets applicable files to “restricted” and creates their non-restricted forms

## Slide 10: Dump Files (cont.)
On WCOSS in:
  /com/NET/prod/RUN.yyyymmdd/MODEL.tcycz.TYPE.tmMM.bufr_d, where:
  NET(RUN/MODEL) is either: cdas(cdas/cdas), cfs(cdas/cdas1), dump(dump/dump), gfs(gdas/gdas1), gfs(gfs/gfs), nam(nam/nam), nam(ndas/ndas), rap(rap/rap), rap(rap_p/rap_p), rtma(rtma/rtma)
  cyc is cycle (hourly for NET=dump, rap, rtma; 00, 06, 12, 18 all others)
  MM is 00 for all types except RUN/MODEL=ndas/ndas where it can be 12, 09, 06 or 03
  TYPE is either: 1bamua, 1bamub, 1bhrs3, 1bhrs4, 1bmhs, adpsfc, adpupa, aircar, aircft, airsev, ascatt, ascatw, atms, atovs, avcsam, avcspm, bathy, cris, esamua, esamub, eshrs3, esmhs, geoimr, goesfv, goesnd, gome, gpsipw, gpsro, lghtng, lgycld, mls, msonet, mtiasi, nexrad, omi, osbuv8, proflr, radwnd, rassda, satwnd, sevcsr, sfcshp, sptrmm, ssmisu, tesac, trkob, trmm, vadwnd, wdsatr, wndsat (types actually dumped depend upon the network)

## Slide 11: PrepBUFR Processing/Files
BUFR
Generated on production WCOSS machine in each network from conventional data dump files
  adpsfc, adpupa, aircar, aircft, ascatw, atovs, goesnd, gpsipw, msonet, proflr, rassda, satwnd (except for GFS/GDAS), sfcshp, vadwnd, wndsat
Network-specific parm cards control processing
Structure defined by input PrepBUFR mnemonic table
BUFR message types can include:
  ADPUPA, AIRCAR, AIRCFT, SATWND, PROFLR, VADWND, SATEMP, ADPSFC, SFCSHP, SFCBOG, SPSSMI, SYNDAT, ERS1DA, GOESND, QKSWND, MSONET, GPSIPW, RASSDA, WDSATR, ASCATW (what is present depends on the network)
  Each message type has its own BUFR structure as defined in the PrepBUFR mnemonic table
Post-processing sets files to restricted, creates non-restricted forms

## Slide 12: PrepBUFR Processing/Files (cont.)
On WCOSS in:
/com/NET/prod/RUN.yyyymmdd/MODEL.tcycz.prepbufr, where:
  NET(RUN/MODEL) is either: akrtma(akrtma/rtma), (cdas(cdas/cdas), cfs(cdas/cdas1), gfs(gdas/gdas1), gfs(gfs/gfs), gurtma(gurtma/gurtma), hirtma(hirtma/rtma), prrtma(prrtma/rtma), rtma2p5(rtma2p5/rtma2p5)
  cyc is cycle (hourly for NET=*rtma*; 00, 06, 12, 18 all others)
On WCOSS in: /com/NET/prod/RUN.yyyymmdd/MODEL.tcycz.prepbufr.tmMM, where:
  NET(RUN/MODEL) is either: nam(nam/nam), nam(ndas/ndas), rap(rap/rap), rap(rap_p/rap_p), rtma(rtma/rtma)
  cyc is cycle (hourly for NET=rap, rtma; 00, 06, 12, 18 all others)
  MM is 00 for all types except RUN/MODEL=ndas/ndas where it can be 12, 09, 06 or 03

## Slide 13: Modules that run as part of the PrepBUFR processing
PREPRO:
  Reads in dumps, parm cards and PrepBUFR mnemonic table. Preforms rudimentary QC. Generates initial (pre-QC) PrepBUFR file.
PREVENT:
  Encodes global guess interpolated to obs locations into PrepBUFR file (used by subsequent QC modules).
    Tropical cyclones may be relocated in guess in upstream processing.
  Encodes observation error into PrepBUFR file (used by GSI).
  Performs some rough quality control checks on surface pressure (vs. the background). Updates are encoded into PrepBUFR file.
VIRTMP
  Converts dry bulb temperature to virtual temperature and dewpoint temperature to specific humidity. Updates are encoded into PrepBUFR file.
SYNDATA [runs in GFS/GDAS (for weak storms with no relocation upstream) and NAM/NDAS (for all storms)]
  Reads in QC’d tropical cyclone records (“tcvitals”). Generates bogused wind profile reports in the vicinity of tropical storms. Generates bogused surface pressure and vertical profile moisture reports at storm center (NAM/NDAS only). Updates are encoded into PrepBUFR file.
  Flags (for non-assimilation) all mass observations in the vicinity of each storm in the tcvitals file list. Updates are encoded into PrepBUFR file.
  Flags (for non-assimilation) all dropwinsonde wind observations in the vicinity of each storm in the tcvitals file list. Updates are encoded into PrepBUFR file.

## Slide 14: Modules that run as part of the PrepBUFR processing (cont.)
CQCHT (does not run in RTMA network)
  Performs complex quality control on rawinsonde heights and temperatures to identify and/or correct location, transcription and communications errors. Erroneous data that cannot be corrected are flagged for non-assimilation. Updates are encoded into PrepBUFR file.
  Checks include hydrostatic, increment, horizontal statistical, vertical statistical, temporal, baseline and lapse rate.
RADCOR (does not run in RTMA network)
  Applies intersonde (radiation) corrections to CQCHT QC’d rawinsonde height and temperature data. The degree of correction is a function of the rawinsonde instrument type, sun angle and pressure level. Updates are encoded into PrepBUFR file.
CQCPROF (does not run in RTMA network)
  Performs complex quality control on wind profiler and SODAR data to identify erroneous data and remove it from consideration by the analyses. Updates are encoded into PrepBUFR file.
  Checks include increment, vertical statistical, temporal statistical, and combined vertical-temporal.
CQCVAD (does not run in RTMA network)
  Performs complex quality control on Velocity Azimuth Display (VAD) winds from WSR-88D radars to identify erroneous data and remove it from consideration by the analyses. Updates are encoded into PrepBUFR file.
  Checks include increment, vertical statistical, temporal statistical, and combined vertical-temporal. In addition, there is an algorithm to account for contamination due to the seasonal migration of birds.

## Slide 15: Modules that run as part of the PrepBUFR processing (cont.)
NRLACQC (does not run in RTMA network)
  Performs quality control on all types of aircraft wind and temperature data. Reports failing QC are flagged if they cannot be rehabilitated. Duplicate reports are removed. Updates are encoded into PrepBUFR file.
  Checks on tracks include duplicate report, spike, invalid data, stuck value, gross, inconsistent altitude or position, flight order, suspect data, reject list. The QC algorithm was developed by the NRL.
OIQC (runs only in GFS & GDAS networks; output is not used by GSI because it performs its own internal QC)
  Performs an OI-based QC on the full set of obs in the PrepBUFR file. A final quality decision is made based on the results from all prior platform-specific quality checks (see above) and from any manual quality marks attached to the data. . Updates are encoded into PrepBUFR file.
  Checks include horizontal, vertical, geostrophic.
The updated observation and quality mark information from the modules listed above is stored in replicated “event stacks”. They are arranged such that the first replication (i.e., the top of the stack) represents the final module’s observation/quality mark update. This is what is read by the analysis.
  If information about previous module updates is needed, the full event stack can be unpacked. This allows one to view the record of every change to an observation throughout the course of the PrepBUFR processing.

## Slide 16: NCEP puts almost all obs into BUFR
Advantages of BUFR:
  Flexibility
  Compact Data Storage
  WMO Standard
Features of NCEP BUFR files:
  Use BUFRLIB routines to interface with files
  BUFR table encoded into “dictionary” messages at top of file
    Files are self defined, no need for external BUFR table to decode
  Uses a single sequence descriptor to define complete subset structure in descriptor section (3) of BUFR messages (more on this later)
  NCEP BUFR adheres to WMO standard

## Slide 17: BUFR File Structure
All BUFR files (including tank, dump and PrepBUFR files) consist of a sequence of “messages”. Each message contains multiple “subsets” (or reports), each with the same structure (usually the same type of data). This structure is actually defined prior to the subsets within each message and consists of a series of “descriptors” whose attributes (e.g., scale, reference value, bit width, units) are defined in a BUFR table. Each subset contains all of the observations plus metadata making up a meteorological report.
(Note: Here, Message 1 BUFR file…
represents the first
“data” message. Recall
that NCEP BUFR files
normally have the
BUFR table encoded
into “dictionary”
messages at their top.)
Message 1
Message 2
…
Message n
Message 1
Subset 1
Subset 2
…
Subset n

## Slide 18: BUFR Tables: Define report structure in an NCEP BUFR file
The structure for the various types of reports/subsets are defined by “NCEP BUFR Mnemonic Table” text files when using the NCEP BUFRLIB software. Again, the tables defining the report structures are encoded in special “dictionary” messages at the top of the file.
An excerpt from PrepBUFR mnemonic table for ADPUPA (upper-air) message type (see http://www.emc.ncep.noaa.gov/mmb/data_processing/Obs_group_roundtable.doc/prepbufr_table.htm)
| ADPUPA | HEADR SIRC {PRSLEVEL} <SST_INFO> <PREWXSEQ> {CLOUDSEQ} |
| ADPUPA | <CLOU2SEQ> <SWINDSEQ> <AFIC_SEQ> <TURB3SEQ> |
SIRC is a mnemonic defining the data (BUFR Table B) descriptor defined as “Solar and infrared radiation correction” (a code table value defined externally).
HEADR, PRSLEVEL, SST_INFO, PREWXSEQ, CLOUDSEQ, CLOU3SEQ, SWINDSEQ, AFIC_SEQ & TURB3SEQ are mnemonics defining sequence (BUFR Table D) descriptors which expand further into other sequence and data mnemonics (see next two slides).
Excellent references for NCEP BUFR TABLES: http://www.nco.ncep.noaa.gov/sib/decoders/BUFRLIB/toc/dfbftab/
http://www.emc.ncep.noaa.gov/mmb/data_processing/NCEP_BUFR_File_Structure.htm

## Slide 20
Here, RED mnemonics represent sequences (BUFR Table D) & GREEN mnemonics represent data values (BUFR Table B).
Here is the same ADPUPA message type as on slide 18, now expanded out to its full set of component data mnemonics:
| ADPUPA | SID XOB YOB DHR ELV TYP T29 TSB ITP SQN PROCN RPT TCOR <RSRD |
| ADPUPA | EXPRSRD> SIRC {CAT <[POB PQM PPC PRC] <POE PFC <PFCMOD>> <PAN |
| ADPUPA | <PCL PCS> POETU PVWTG PVWTA>> <[QOB QQM QPC QRC] TDO <QOE QFC |
| ADPUPA | <QFCMOD>> <QAN <QCL QCS> QOETU QVWTG QVWTA ESBAK>> <[TOB TQM TPC |
| ADPUPA | TRC] TVO <TOE TFC <TFCMOD>> <TAN <TCL TCS> TOETU TVWTG TVWTA>> |
| ADPUPA | <[ZOB ZQM ZPC ZRC] <ZFC <ZFCMOD>> <ZAN <ZCL ZCS>>> <[UOB VOB WQM |
| ADPUPA | WPC WRC] [DDO FFO DFQ DFP DFR] <WOE UFC VFC <UFCMOD VFCMOD>> <UAN |
| ADPUPA | VAN <UCL UCS VCL VCS> WOETU WVWTG WVWTA RF10M >> <XDR YDR HRDR>} |
| ADPUPA | <[SST1 SSTQM SSTPC SSTRC] MSST <SSTOE SSTFC> <SSTAN> <DBSS>> |
| ADPUPA | <PRWE> {VSSO CLAM CLTP HOCB <HOCT>} <TOCC HBLCS> <WDIR1 WSPD1> |
| ADPUPA | <AFIC HBOI HTOI> <DGOT HBOT HTOT> |
It is long and detailed! The NCEP BUFRLIB compacts this into just the single descriptor defining the sequence mnemonic
“ADPUPA”. Thus, only one value is encoded in the descriptor section (3) of each ADPUPA BUFR message!

## Slide 21: Replication: efficient data storage in BUFR
Two main types of replication:
  Fixed (or standard): the number of repetitions for a given sequence is always known ahead of time and is the same for every subset in a message
    Example: satellite data from a fixed number of channels; a set number of quality marks
  Delayed: the number of repetitions for a given sequence is not known ahead of time and may vary for subsets in a message
    Example: pressure levels in a radiosonde report
Only sequence mnemonics can be replicated in NCEP BUFRLIB!

## Slide 22: Standard Replication/NCEP BUFR
A sequence that is repeated a fixed number of times appears in the BUFR tables surrounded by quotation marks followed by the number of replications
  Example: GOES IR winds
  | NC005015 | BID RCPTIM RPID CORN |
  | NC005015 | SAID OGCE SCLF SAZA SSNX SSNY |
  | NC005015 | YEAR MNTH DAYS HOUR MINU SECO TPHR CLAT CLON |
  | NC005015 | SIDP SWCM SCCF SCBW CCST TCMD LSQL OFGI SWQM |
  | NC005015 | HAMD PRLC |
  | NC005015 | WDIR "GQCPRMS"3 |
  | NC005015 | WSPD "GQCPRMS"3 |
  | NC005015 | "TWIND"4 |
  | NC005015 | "MDPT"10 |
  | GQCPRMS | OGCE GNAP PCCF |
  Here, sequence GQCPRMS (OGCE GNAP PCCF) is repeated 3 times.
  OGCE = Originating Center
  GNAP = Generating Application
  PCCF = Percent Confidence
Fixed replication appears rarely, if ever, in the PrepBUFR table. However, it does occur in many of the tank and dump tables.

## Slide 23: Delayed Replication/NCEP BUFR
< SEQ_MNEMONIC >  one-bit delayed replication:
The sequence is repeated either zero or one time(s)
Represents a way to turn “on” or “off” a set of data values in the sequence
Only 1 bit is needed to represent all data values in the sequence being missing (0 replications) rather than filling each value in the sequence with all bits “on” (which represents missing in BUFR)
  This is an efficient way to store data sequences that are always missing (e.g., PIBAL mass data in ADPUPA message type )
{ SEQ_MNEMONIC } or [ SEQ_MNEMONIC ]  8-bit delayed replication:
The sequence can be repeated up to 255 times
{ } represent regular data replications (e.g., profile levels, radiance channels)
[ ] represent replicated (stacked) “events” (only in PrepBUFR files)
  Each event normally consists of a sequence representing the obs value & its quality mark, along with a program code & a reason code (providing metadata on what module updated the obs/quality mark and why it did what it did)
{ } and [ ] replications are treated differently by the BUFRLIB software
( SEQ_MNEMONIC )  16-bit delayed replication:
Like { } except the sequence can be repeated up to 65,535 times

## Slide 24: PrepBUFR event stacks: Previous example of ADPUPA message type

## Slide 25: Commonly Used BUFRLIB Routines
openbf
readmg/ireadmg
readsb/ireadsb
openmb
ufbint
ufbevn
ufbrep
ufbseq
writsb
closbf
Detailed documentation of the use of these and other routines is available at http://www.nco.ncep.noaa.gov/sib/decoders/BUFRLIB/

## Slide 26: NCEP BUFRLIB Software
A simple overview is presented in these slides. For more details, see http://www.nco.ncep.noaa.gov/sib/decoders/BUFRLIB/
  Quality reference for:
    Purposes/specific uses of major BUFRLIB routines
    BUFRLIB routine arguments
Some preliminary information:
  Previous versions of BUFRLIB required BUFR files to be FORTRAN-blocked
  The newest version (updated for the NCEP supercomputer move from CCS to WCOSS) will work with EITHER blocked or unblocked BUFR files
    On WCOSS, all BUFR files are now unblocked (the default)

## Slide 27: Pseudo-code for READING
call openbf ! Open BUFR file for reading
do while(ireadmg.eq.0) ! Sequentially read in each BUFR message in the file
do while(ireadsb.eq.0) ! Sequentially read in each subset in the current message
depending on data types and their report structures, call either:
      ufbint
      ufbevn
      ufbrep
      ufbseq
    these routines pull data values from subsets in the BUFR file
enddo ! ireadsb
enddo ! ireadmg
call closbf ! All messages and subsets read from BUFR file, close it
(for more information, see
http://www.emc.ncep.noaa.gov/mmb/data_processing/decode_only_BUFR_example.txt)

## Slide 28: Pseudo-code for WRITING
call openbf ! Open BUFR file for writing
do while … ! Loop through each native-format “report” that is to be encoded into the BUFR file
put report into arrays that allow it to interface with BUFRLIB software
call openmb ! Opens a new BUFR message in output file for writing (if necessary)
depending on data types and their report structures, call either:
  ufbint
  ufbrep
  ufbseq
  these routines store data values for report into BUFRLIB memory
call writsb ! Encode report into BUFR message in output file
enddo ! while …
call closbf ! All subsets written into BUFR file, close it
(for more information, see
http://www.emc.ncep.noaa.gov/mmb/data_processing/encode_only_BUFR_example.txt)

## Slide 29: Appending data to an existing PrepBUFR file
Before appending any new data to a PrepBUFR file, examine its BUFR table.
Make sure the report structure in the existing file fits the report structure of the data you want to append. The report structure in the table can change from time to time as new variables get added. The report structures in the table used to build the original BUFR file should match the report structures of the data you want to add. If not, you may get errors later when using BUFRLIB to decode the data in the file.
If you’re not sure of the report structures within the PrepBUFR file, you can use the BUFRLIB routine dxdump to extract the table from the dictionary messages at the top of the file.
call dxdump(lun,outlun)
See http://www.nco.ncep.noaa.gov/sib/decoders/BUFRLIB/toc/other/#dxdump
for more details.
Unit number connected to the PrepBUFR file
Unit number connected to a text file for output

## Slide 30: Appending data to an existing PrepBUFR file (cont.)
The main coding difference between creating a new PrepBUFR file and appending data to an existing file lies in the second argument to the BUFRLIB subroutine openbf (open BUFR file):
! Create a new BUFR file for output
call openbf(<unit number connected to PrepBUFR file>,'OUT',<unit number connected to PrepBUFR table>)
vs.
! Append data to an existing BUFR file
call openbf(<unit number connected to PrepBUFR file>,‘APX',<unit number connected to PrepBUFR table>)
See http://www.nco.ncep.noaa.gov/sib/decoders/BUFRLIB/toc/intro/#openbf
for more details.

## Slide 31: Online sources of help and information
NCO BUFRLIB Documentation: http://www.nco.ncep.noaa.gov/sib/decoders/BUFRLIB/
WMO General BUFR Docs: http://www.wmo.int/pages/prog/www/WMOCodes/Guides/BUFRCREXPreface_en.html
Obs/QC Processing Forum (including BUFR): http://emc-ls-sand04.ncep.noaa.gov/forum/viewforum.php?f=25&sid
- may need to be inside NCEP firewall for access
EMC Docs:
Overall description of how data is processed at NCEP: http://www.emc.ncep.noaa.gov/mmb/data_processing/data_processing/
“Table B” (defines mnemonics that represent various data values): http://www.emc.ncep.noaa.gov/mmb/data_processing/bufrtab_tableb.htm

## Slide 32: What if the online docs don’t answer your question?
Some problems and challenges faced by those working with files in BUFR format are best handled on a case-by-case basis.
How to get help and information:
BUFRLIB support via online web form: http://www.nco.ncep.noaa.gov/sib/decoders/mail_bufrlib/
Comments and questions sent via this form reach key contacts in EMC and NCO. Exchanges are then made via email to solve problems.

## Slide 33: In a nutshell…
The BUFR format for meteorological data is flexible and powerful but sometimes confusing for new (and even experienced!) users.
NCEP uses the BUFRLIB software and BUFR tables to interact with BUFR files (including PrepBUFR files).
Working with BUFR files requires some patience, especially at first.
Often, BUFR and the BUFRLIB software are easiest to learn by:
  working through examples
  experimentation
  not being afraid to dig in and try out your own code
Help is available! Most experienced users still remember the growing pains they felt while learning to use BUFR. Please ask for help if you need it!

## Slide 34
Questions?