NCEP SUPEROB LEVEL 2.5 DOCUMENTATION

Updated  January 28, 2010

Figure 3-X.  	SuperOb Wind Data Packet (Sheet 1 of 2)

| FIELDNAME | TYPE | UNITS | RANGE | PRECISION/ ACCURACY | REMARKS |
| --- | --- | --- | --- | --- | --- |
| Packet Code | INT*2 | N/A | 27 | N/A | Packet Type 27 |
| Length of Packet | INT*4 | Bytes | 2 to 324002 | 1 | Number of bytes to follow in this packet (including elevation angle) |
| Elevation Angle | INT*2 | Degrees | -1.0 to +45.0 | 0.1 | Angle of the Elevation Scan |
| Latitude | INT*4 | Degrees | -90 to +90 | 0.001 | North(+) or South(-) of the Equator of the SuperOb cell |
| Longitude | INT*4 | Degrees | -180 to +180 | 0.001 | East(+) or West(-) of the Prime Meridian of the SuperOb cell |
| Height | INT*2 | Meters | -100 to 21336 | 1 | Height above MSL of the SuperOb cell |
| Average Radial Velocity | INT*2 | Meters/ Second | -127 to +126 | 0.01 | Average radial velocity of the SuperOb cell |
| Standard Dev. Of Ave. Radial Velocity | INT*2 | Meters/ Second | 0 to 255 | 1 | Standard deviation of the radial velocities in the SuperOb cell |
| Time Deviation | INT*2 | Seconds | -5400 to +5400 | 1 | Deviation from Base Time of the average time of all velocity samples in the SuperOb cell |
| Azimuth Average | INT*2 (Note 1) | Degrees | 0 to 359 | 0.01 | Average azimuth angle of all velocity samples in the SuperOb cell. |

Note 1:  The Azimuth Average field is an unsigned 16-bit value.

Figure 3-X.  	SuperOb Wind Data Packet (Sheet 2 of 2)

The description about the use of level 2.5 Superob data is discussed in detail in an article entitled “ Radial Wind Super-Obs from the WSR-88D Radars in the NCEP Operational Assimilation System” by Jordan C. Alpert and V. Krishna Kumar, Monthly Weather Review, Volume 135, pp 1090-1109, 2007.

The Superob level 2.5 data format is provided by the NWS Radar Operations Center (ROC).

/*12345678912345678912345678912345678912345678912345678912345678*/

/*								*/

/* read_superob.h --- header file for read_superob.c		*/

/* author: Yukuan Song						*/

/* version: 1.0							*/

/* time: May 31, 2002						*/

/*								*/

/****************************************************************/

#ifndef READ_SUPEROB_H

#define READ_SUPEROB_H

typedef struct {   /* message header block 			*/

short msg_code;/* message code: -131 - -16; 0 - 211 	*/

short date;    /* date of the message; modified Julian date */

int time;      /* time of the message; GMT; seconds after

midnight, 1/1/1970 			*/

int length;    /* message length; number of bytes including

this header; Note that this is the length

in the C structure format. 		*/

short src_id;  /* ID of the sender: 0 - 999 		*/

short dest_id; /* ID of the receiver: 0 - 999 		*/

short n_blocks;/* header block plus the product description

blocks in the message 			*/

short divider;	/* value of -1 used to delineate the header from

the above message header; DIV1OFF 10 */

int latitude;	/* latitude of radar in .001 degrees, -90. - 90.;

LTMSWOFF LTLSWOFF */

int longitude;	/* longitude of radar in .001 degrees,

-180. - 180. East (+) and West (-); LNMSWOFF

LNLSWOFF */

short height;	/* above mean sea level height of radar in feet,

-100 - 11000 RADHGTOFF */

short prod_code;	/* Internel product code; 16 - 131; negative

number is used sometimes; the same as msg_code?;

PRDCODOFF 16 */

short op_mode;	/* operational (weather) mode; 0 = maintenance;

1 = clear air; 2 = precipitation (severe weather);

WTMODOFF */

short vcp_num;	/* VCP number; 1 - 767; VCPOFF */

short seq_num;	/* sequence number of the request that generated

the product (refer to figure 3-3, RPG/PUP ICD);

for products generated by an alert condition,

= -13; SQNUMOFF */

short vol_num;	/* counter, recycles to one (1) every 80 volume

scans; 1 - 80, VSNUMOFF */

short vol_date;	/* Modified Julian date; VSDATOFF */

short vol_time_s;	/* number of seconds after midnight GMT		*/

unsigned short vol_time_l;/* number of seconds after midnight GMT		*/

short gen_date;	/* product generation data; modified Julian date;

GDPRDOFF */

int gen_time;	/* product generation time; seconds after

midnight GMT; GTMSWOFF GTLSWOFF */

short base_time;	/* base time -- center of time window    	*

* minutes from midnight 			*/

short time_radius;	/* time radius of time window			*/

short elev_ind;	/* RPG elevation index in a volume (not cut number);

1 - 20; ELINDOFF */

short param_3;	/* product dependent parameter.  For products

16 - 21, 28 - 30, 22 - 27, 49, 88, 87, 43, 46,

45, 44, 55, 56, elevation angle; in .1 degrees;

-1.0 - 45.0; for product 84; horizontal wind

altitude in 1000 feet, ; 0 to 70; EAZALOFF 30 */

short level_1;	/* data lev. thre. (see p3-63, PRG/PUP ICD);

DL1OFF 31 */

short level_2;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL2OFF */

short level_3;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL3OFF */

short level_4;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL4OFF */

short level_5;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL5OFF */

short level_6;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL6OFF */

short level_7;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL7OFF */

short level_8;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL8OFF */

short level_9;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL9OFF */

short level_10;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL10OFF */

short level_11;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL11OFF */

short level_12;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL12OFF */

short level_13;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL13OFF */

short level_14;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL14OFF  */

short level_15;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL15OFF*/

short level_16;	/* data lev. thre. (see p3-63, PRG/PUP ICD);

DL16OFF 46 */

short cell_range_size;/* size of each cell range in km		*/

short cell_azimuth_size;/* size of each cell azimuth in degree	*/

short maximum_range;/* maximum range from the radar km		*/

short min_num_points;/* minimum number of points in each cell	*/

short param_8;

short param_9;	/* product dependent parameters.

product: 16 - 21, 39 - 40, 35 - 38, 50, 85, 63,

65, 64, 66, 89, 90, calibration constant;

in dB; -50. - 50.; CALCONMSW 51 CALCONLSW

product: 81; cast to short; rainfall endtime;

minutes; 0 - 1439;

product: 74; cast to short; edited indicator;

not 0 for edited;

product: 43, 46, 45, 44, ; cast to short;

alert category; see table IV;

product: 55; cast to two shorts;

storm speed; .1 Knots; 0 - 99.9;

storm direction; .1 degrees; 0 - 359.9;

product: 56; cast to two shorts;

average storm speed; .1 Knots; 0 - 99.9;

average storm direction; .1 degrees; 0 - 359.9;

product: 80; cast to two shorts;

end time rainfall; minutes; 0 - 1439;

rate bias; in .01; 0 - 99.99;

product: 78, 79; cast to short; rainfall end time;

in minutes; 0 - 1439;

product: 84; cast to short; RMS error; Knots;

0 - 29; STSPDOFF 51 STDIROFF 52 */

short param_10;	/* product dependent parameter.

product: 39, 40, ; contour interval; dBZ; 5 - 25;

product: 42; contour interval; feet; 2000 - 30000;

product: 53; alert catagory; see table IV;

product: 80; error var of bias; in .01; 0 - 99.99;

CNTINTOFF 53 */

short n_maps;	/* if the message is a map data, this is the number

of map pieces, otherwise it is 0; 0 - 17;

NMAPSOFF 54 */

int sym_off;	/* number of shorts from the top of message (message

code field in header) to the -1 divider of each

block listed. If the offset is zero, the block is

not part of the product in question;

OPRMSWOFF 55 OPRLSWOFF 56 */

int gra_off;	/* same as above to graphic block

OGMSWOFF 57 OGLSWOFF 58 */

int tab_off;	/* same as above to tabular block

OTADMSWOFF 59 OTADLSWOFF 60 */

} Msg_header_pdb;

typedef struct {

short divider;	/* value of -1 used to delineate the following from

the above product description block; DIV2OFF 61 */

short block_id;	/* always 1 */

int block_len;	/* length of this block in bytes including the

preceding devider and block id; 1 - 80000 */

short n_layers;	/* number of data layers obtained in this block;

1 - 15 */

short layer_divider;/* value of -1 used to delineate one data layer

from another; */

int data_len;	/* length of data layer (in bytes) starting from the

bytes after this int and ending at the last data

of this layer; 1 - 80000; */

} Symbology_block_header;

#endif

/*12345678912345678912345678912345678912345678912345678912345678*/

/*								*/

/* read_superob.h --- header file for read_superob.c		*/

/* author: Yukuan Song						*/

/* version: 1.0							*/

/* time: May 31, 2002						*/

/*								*/

/****************************************************************/

#ifndef READ_SUPEROB_H

#define READ_SUPEROB_H

typedef struct {   /* message header block 			*/

short msg_code;/* message code: -131 - -16; 0 - 211 	*/

short date;    /* date of the message; modified Julian date */

int time;      /* time of the message; GMT; seconds after

midnight, 1/1/1970 			*/

int length;    /* message length; number of bytes including

this header; Note that this is the length

in the C structure format. 		*/

short src_id;  /* ID of the sender: 0 - 999 		*/

short dest_id; /* ID of the receiver: 0 - 999 		*/

short n_blocks;/* header block plus the product description

blocks in the message 			*/

short divider;	/* value of -1 used to delineate the header from

the above message header; DIV1OFF 10 */

int latitude;	/* latitude of radar in .001 degrees, -90. - 90.;

LTMSWOFF LTLSWOFF */

int longitude;	/* longitude of radar in .001 degrees,

-180. - 180. East (+) and West (-); LNMSWOFF

LNLSWOFF */

short height;	/* above mean sea level height of radar in feet,

-100 - 11000 RADHGTOFF */

short prod_code;	/* Internel product code; 16 - 131; negative

number is used sometimes; the same as msg_code?;

PRDCODOFF 16 */

short op_mode;	/* operational (weather) mode; 0 = maintenance;

1 = clear air; 2 = precipitation (severe weather);

WTMODOFF */

short vcp_num;	/* VCP number; 1 - 767; VCPOFF */

short seq_num;	/* sequence number of the request that generated

the product (refer to figure 3-3, RPG/PUP ICD);

for products generated by an alert condition,

= -13; SQNUMOFF */

short vol_num;	/* counter, recycles to one (1) every 80 volume

scans; 1 - 80, VSNUMOFF */

short vol_date;	/* Modified Julian date; VSDATOFF */

short vol_time_s;	/* number of seconds after midnight GMT		*/

unsigned short vol_time_l;/* number of seconds after midnight GMT		*/

short gen_date;	/* product generation data; modified Julian date;

GDPRDOFF */

int gen_time;	/* product generation time; seconds after

midnight GMT; GTMSWOFF GTLSWOFF */

short base_time;	/* base time -- center of time window    	*

* minutes from midnight 			*/

short time_radius;	/* time radius of time window			*/

short elev_ind;	/* RPG elevation index in a volume (not cut number);

1 - 20; ELINDOFF */

short param_3;	/* product dependent parameter.  For products

16 - 21, 28 - 30, 22 - 27, 49, 88, 87, 43, 46,

45, 44, 55, 56, elevation angle; in .1 degrees;

-1.0 - 45.0; for product 84; horizontal wind

altitude in 1000 feet, ; 0 to 70; EAZALOFF 30 */

short level_1;	/* data lev. thre. (see p3-63, PRG/PUP ICD);

DL1OFF 31 */

short level_2;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL2OFF */

short level_3;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL3OFF */

short level_4;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL4OFF */

short level_5;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL5OFF */

short level_6;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL6OFF */

short level_7;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL7OFF */

short level_8;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL8OFF */

short level_9;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL9OFF */

short level_10;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL10OFF */

short level_11;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL11OFF */

short level_12;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL12OFF */

short level_13;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL13OFF */

short level_14;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL14OFF  */

short level_15;	/* data lev. thre. (see p3-63, PRG/PUP ICD) DL15OFF*/

short level_16;	/* data lev. thre. (see p3-63, PRG/PUP ICD);

DL16OFF 46 */

short cell_range_size;/* size of each cell range in km		*/

short cell_azimuth_size;/* size of each cell azimuth in degree	*/

short maximum_range;/* maximum range from the radar km		*/

short min_num_points;/* minimum number of points in each cell	*/

short param_8;

short param_9;	/* product dependent parameters.

product: 16 - 21, 39 - 40, 35 - 38, 50, 85, 63,

65, 64, 66, 89, 90, calibration constant;

in dB; -50. - 50.; CALCONMSW 51 CALCONLSW

product: 81; cast to short; rainfall endtime;

minutes; 0 - 1439;

product: 74; cast to short; edited indicator;

not 0 for edited;

product: 43, 46, 45, 44, ; cast to short;

alert category; see table IV;

product: 55; cast to two shorts;

storm speed; .1 Knots; 0 - 99.9;

storm direction; .1 degrees; 0 - 359.9;

product: 56; cast to two shorts;

average storm speed; .1 Knots; 0 - 99.9;

average storm direction; .1 degrees; 0 - 359.9;

product: 80; cast to two shorts;

end time rainfall; minutes; 0 - 1439;

rate bias; in .01; 0 - 99.99;

product: 78, 79; cast to short; rainfall end time;

in minutes; 0 - 1439;

product: 84; cast to short; RMS error; Knots;

0 - 29; STSPDOFF 51 STDIROFF 52 */

short param_10;	/* product dependent parameter.

product: 39, 40, ; contour interval; dBZ; 5 - 25;

product: 42; contour interval; feet; 2000 - 30000;

product: 53; alert catagory; see table IV;

product: 80; error var of bias; in .01; 0 - 99.99;

CNTINTOFF 53 */

short n_maps;	/* if the message is a map data, this is the number

of map pieces, otherwise it is 0; 0 - 17;

NMAPSOFF 54 */

int sym_off;	/* number of shorts from the top of message (message

code field in header) to the -1 divider of each

block listed. If the offset is zero, the block is

not part of the product in question;

OPRMSWOFF 55 OPRLSWOFF 56 */

int gra_off;	/* same as above to graphic block

OGMSWOFF 57 OGLSWOFF 58 */

int tab_off;	/* same as above to tabular block

OTADMSWOFF 59 OTADLSWOFF 60 */

/*

C$$$  MAIN PROGRAM DOCUMENTATION BLOCK

C

C MAIN PROGRAM:  RADAR_UNCOMP_SUP2P5

C   PRGMMR: KUMAR            ORG: NP12        DATE: 2004-07-02

C

C ABSTRACT: READS IN FILES CONTAINING LEVEL 2.5 SINGLE STATION HOURLY SUPEROB

C   REPORTS AND UNCOMPRESSES THEM.

C

C PROGRAM HISTORY LOG:

C 2002-05-31  YUKUAN SONG      -- ORIGINAL AUTHOR

C 2004-07-02  V. KRISHNA KUMAR -- PREPARED FOR IMPLEMENTATION

C

C USAGE:

C   INPUT FILES:

C     $filename - UNCOMPRESSED FILE

C

C   OUTPUT FILES:

C     $filename.uncompress.out - STANDARD OUTPUT

C     $filename.uncom - UNCOMPRESSED FILE

C

C   SUBPROGRAMS CALLED:

C     UNIQUE:    - DECOMPRESS BLOCKSORT COMPRESS CRCTABLE HUFFMAN RANDTABLE

C     LIBRARY:

C       BZIP2LIB - BZLIB

C

C   EXIT STATES:

C     COND =   0 - SUCCESSFUL RUN

C            > 0 - ABNORMAL RUN

C

C REMARKS: NONE.

C

C ATTRIBUTES:

C   LANGUAGE: C

C   MACHINE:  IBM CCS

C

C$$$

*/

/*1234567891234567891234567891234567891234567891234567891234567891234567*/

/*									*/

/* superob2.5_read_uncompress.c --- read SuperOb2.5 Product             */

/* author: Yukuan Song 							*/

/* version: 1.0								*/

/* time: May 31, 2002							*/

/* Contact: Yukuan.Song@noaa.gov                                        */

/* Program was tested for generating bufr data into dcomdev tanks       */

/* by V. Krishna Kumar W/NP12 Data Management & Qual. Assess. Branch    */

/*									*/

/************************************************************************/

#include <stdio.h>    /* declare FILE data type				*/

#include <stdlib.h>   /* declare for malloc                             */

#include <string.h>    /* declare string data type			*/

#include "read_superob.h" /* local header file				*/

#define BZIP2_NOT_SMALL 0

#define BZIP2_NOT_VERBOSE 0

/* declare local variables						*/

FILE *in_fp, *ou_fp, *ou_uncom_fp; /* in_fp points to input file; 			*

* ou_fp points to output file			*/

Msg_header_pdb hr;   /* message header and product description block   *

* total 18+102 = 120 bytes			*/

Symbology_block_header sym_hr; /* Symbology block header               */

int TEST = 1;        /* If 1, print out debug information              */

int count;           /*  count how much data have not bee read yet     */

int i;               /*   an index for the for loop		    	*/

int vol_time;        /* volume scan time				*/

int PRE_HEADER =1;   /* true (1) mean data has a pre_header            */

int offset = 0;     /* offset for buffer dest_buf			*/

/* these varaibles will be used to decompress the data			*/

int ret;

unsigned int dest_len, src_len, buf_alloc = 0;

unsigned short alg;

char *dest_buf=NULL, *prod_data = NULL;

/* Main drive function 							*/

int

main (int argc, char *argv[]) {

/* make sure the command lines are correct				*/

if (argc != 3) {

printf("Usage: a.out input_file out_put_file\n");

return 0;

}

/* Open in_fp file to read, ou_fp to write				*/

if((in_fp = fopen(argv[1], "r")) == NULL) {

printf("Couldn't open %s for read\n", argv[1]);

return 0;

}

else {

if ((ou_fp = fopen(argv[2],"w")) == NULL) {

printf("Couldn't open %s for writing\n", argv[2]);

return 0;

}

}

/* Skip the first 96 bytes which is a pre-header if PRE_HEADER true	*/

if(PRE_HEADER)

fseek(in_fp, 30, 0);

/* Read Message header : Message header + PDB					*/

if( fread(&hr, sizeof(Msg_header_pdb), 1, in_fp) != 1) {

printf("Couldn't read msg header  or pdb form %s\n", argv[1]);

return 0;

}

else {

fprintf(ou_fp, "----------Message Header-------------------------\n");

fprintf(ou_fp, "msg_code=%hd\n", hr.msg_code);

fprintf(ou_fp, "date=%hd\n", hr.date);

fprintf(ou_fp, "time=%d\n", hr.time);

fprintf(ou_fp, "length=%d\n", hr.length);

fprintf(ou_fp, "src_id=%hd\n", hr.src_id);

fprintf(ou_fp, "dest_id=%hd\n", hr.dest_id);

fprintf(ou_fp, "n_blocks=%hd\n\n", hr.n_blocks);

fprintf(ou_fp, "----------Product description block----------\n");

fprintf(ou_fp, "divider=%hd\n", hr.divider);

fprintf(ou_fp, "latitude=%d\n", hr.latitude);

fprintf(ou_fp, "longitude=%d\n", hr.longitude);

fprintf(ou_fp, "height=%hd\n", hr.height);

fprintf(ou_fp, "product_code=%hd\n", hr.prod_code);

fprintf(ou_fp, "op_mode=%hd\n", hr.op_mode);

fprintf(ou_fp, "vcp_num=%hd\n", hr.vcp_num);

fprintf(ou_fp, "seq_num=%hd\n", hr.seq_num);

fprintf(ou_fp, "vol_num=%hd\n", hr.vol_num);

fprintf(ou_fp, "vol_date=%hd\n", hr.vol_date);

vol_time = hr.vol_time_s;

vol_time <<=16;

vol_time |=hr.vol_time_l;

fprintf(ou_fp, "vol_time = %d\n", vol_time);

fprintf(ou_fp, "gen_date=%hd\n", hr.gen_date);

fprintf(ou_fp, "gen_time=%d\n", hr.gen_time);

fprintf(ou_fp, "base_time=%hd\n", hr.base_time);

fprintf(ou_fp, "time_radius=%hd\n", hr.time_radius);

fprintf(ou_fp, "elev_ind=%hd\n", hr.elev_ind);

fprintf(ou_fp, "param_3=%hd\n", hr.param_3);

fprintf(ou_fp, "lelev_1=%hd\n", hr.level_1);

fprintf(ou_fp, "lelev_2=%hd\n", hr.level_2);

fprintf(ou_fp, "lelev_3=%hd\n", hr.level_3);

fprintf(ou_fp, "lelev_4=%hd\n", hr.level_4);

fprintf(ou_fp, "lelev_5=%hd\n", hr.level_5);

fprintf(ou_fp, "lelev_6=%hd\n", hr.level_6);

fprintf(ou_fp, "lelev_7=%hd\n", hr.level_7);

fprintf(ou_fp, "lelev_8=%hd\n", hr.level_8);

fprintf(ou_fp, "lelev_9=%hd\n", hr.level_9);

fprintf(ou_fp, "lelev_10=%hd\n", hr.level_10);

fprintf(ou_fp, "lelev_11=%hd\n", hr.level_11);

fprintf(ou_fp, "lelev_12=%hd\n", hr.level_12);

fprintf(ou_fp, "lelev_13=%hd\n", hr.level_13);

fprintf(ou_fp, "lelev_14=%hd\n", hr.level_14);

fprintf(ou_fp, "lelev_15=%hd\n", hr.level_15);

fprintf(ou_fp, "lelev_16=%hd\n", hr.level_16);

fprintf(ou_fp, "cell_range_size=%hd\n", hr.cell_range_size);

fprintf(ou_fp, "cell_azimuth_size=%hd\n", hr.cell_azimuth_size);

fprintf(ou_fp, "maximum_range=%hd\n", hr.maximum_range);

fprintf(ou_fp, "min_num_points=%hd\n", hr.min_num_points);

fprintf(ou_fp, "param_8=%hd\n", hr.param_8);

fprintf(ou_fp, "param_9=%hd\n", hr.param_9);

fprintf(ou_fp, "param_10=%hd\n", hr.param_10);

fprintf(ou_fp, "n_maps=%hd\n", hr.n_maps);

fprintf(ou_fp, "sym_off=%d\n", hr.sym_off);

fprintf(ou_fp, "gra_off=%d\n", hr.gra_off);

fprintf(ou_fp, "tab_off=%d\n", hr.tab_off);

}

/* Test to see if the product is compressed					*/

if(hr.param_8 == 1){

printf("Data is a bzip2-compressed data; uncompressing first ....\n");

/* Open a file to output uncompressed data					*/

if ((ou_uncom_fp = fopen(strcat(argv[1],".uncom"),"w")) == NULL) {

printf("Couldn't open %s for writing\n", argv[2]);

return 0;

}

/* Find the original and compressed size of the product.                       */

src_len = (unsigned int) (hr.length - sizeof(Msg_header_pdb));

dest_len = ( (unsigned int) (hr.param_9 & 0xffff) << 16) +

(unsigned int) (hr.param_10 & 0xffff);

prod_data = (char *)malloc(src_len);

/* read the whole symbology block compressed					*/

if( fread(prod_data, src_len, 1, in_fp) != 1) {

printf("Couldn't read compressed symbology block \n");

return 0;

}

dest_buf = (char *)malloc( dest_len );

if( dest_buf == NULL ){

printf("malloc Failed For %d Bytes\n", dest_len );

return 0;

}

/* Do the bzip2 decompression. */

ret = BZ2_bzBuffToBuffDecompress( dest_buf,

&dest_len, prod_data, (unsigned int) src_len,

BZIP2_NOT_SMALL, BZIP2_NOT_VERBOSE );

/* update paramter 8 and msg_len in the header				*/

hr.param_8 =0;

hr.length = dest_len+sizeof(Msg_header_pdb);

/* write the header to ou_uncom_fp file				*/

if(fwrite(&hr, sizeof(Msg_header_pdb), 1, ou_uncom_fp) !=1) {

printf("Couldn't write Msg_header_pdb out\n");

return 0;

}

/* write Superob data packet to ou_uncom_fp file			*/

if(fwrite(dest_buf, dest_len, 1, ou_uncom_fp) !=1) {

printf("Couldn't write Superob data packet out\n");

return 0;

}

}

else { /* the data hasn't been compressed				*/

dest_len = (unsigned int) (hr.length - sizeof(Msg_header_pdb));

dest_buf = (char *)malloc( dest_len );

if( dest_buf == NULL ){

printf("malloc Failed For %d Bytes\n", dest_len );

return 0;

<Krishna.Kumar@noaa.gov>

}

printf("dest_len = %u\n", dest_len);

if(fread(dest_buf, dest_len, 1, in_fp) != 1) {

printf("Couldn't read compressed symbology block \n");

return 0;

}

}

/* Read symbology block header -- 16 bytes                                     */

memcpy(&sym_hr, dest_buf+offset, sizeof(Symbology_block_header));

offset +=sizeof(Symbology_block_header);

fprintf(ou_fp, "-------------Symbology block header ---------------\n");

fprintf(ou_fp, "sym_divider=%hd\n", sym_hr.divider);

fprintf(ou_fp, "block_id=%hd\n", sym_hr.block_id);

fprintf(ou_fp, "block_len=%d\n", sym_hr.block_len);

fprintf(ou_fp, "n_layers=%hd\n", sym_hr.n_layers);

fprintf(ou_fp, "layer_divider=%hd\n", sym_hr.layer_divider);

fprintf(ou_fp, "data_len=%d\n", sym_hr.data_len);

/* Read the Superob Wind Data Packet					*/

{

short packet_code;      /* packet code = 27				*/

int   packet_len;       /* length of superob data packet              */

short elev_angle;       /* elevation angle				*/

int   lat;		  /* latitude					*/

int   longitude;	  /* longitude					*/

short height;           /* height of observation			*/

short mean_w;		  /* mean wind					*/

short std_w;            /* Standard deviation				*/

short time_d;		  /* time deviation				*/

short mean_azimuth;     /* averaged azimuth				*/

memcpy(&packet_code, dest_buf+offset, sizeof(short));

offset +=sizeof(short);

memcpy(&packet_len, dest_buf+offset, sizeof(int));

offset +=sizeof(int);

memcpy(&elev_angle, dest_buf+offset, sizeof(short));

offset +=sizeof(short);

fprintf(ou_fp, "-------------data packet: elevation=%hd-------\n", elev_angle);

fprintf(ou_fp, "packet_code = %hd\n", packet_code);

fprintf(ou_fp, "packet_len = %d\n", packet_len);

fprintf(ou_fp, "elev_angle = %hd\n", elev_angle);

while(offset < dest_len) {

for(i =2; i< packet_len; i+=18) {

memcpy(&lat, dest_buf+offset, sizeof(int));

offset += sizeof(int);

memcpy(&longitude, dest_buf+offset, sizeof(int));

offset += sizeof(int);

memcpy(&height, dest_buf+offset, sizeof(short));

offset += sizeof(short);

memcpy(&mean_w, dest_buf+offset, sizeof(short));

offset += sizeof(short);

memcpy(&std_w, dest_buf+offset, sizeof(short));

offset += sizeof(short);

memcpy(&time_d, dest_buf+offset, sizeof(short));

offset += sizeof(short);

memcpy(&mean_azimuth, dest_buf+offset, sizeof(short));

offset += sizeof(short);

fprintf(ou_fp,"lat= %d\n", lat);

fprintf(ou_fp,"longitude= %d\n", longitude);

fprintf(ou_fp,"height= %d\n", height);

fprintf(ou_fp,"mean_w= %hd\n", mean_w);

fprintf(ou_fp,"std_w= %hd\n", std_w);

fprintf(ou_fp,"time_d= %hd\n", time_d);

fprintf(ou_fp,"mean_azimuth= %hu\n", mean_azimuth);

} /* END of for(i=0; i< packet_len....)				*/

if(offset <dest_len) {

memcpy(&packet_code, dest_buf+offset, sizeof(short));

offset +=sizeof(short);

memcpy(&packet_len, dest_buf+offset, sizeof(int));

offset +=sizeof(int);

memcpy(&elev_angle, dest_buf+offset, sizeof(short));

offset +=sizeof(short);

fprintf(ou_fp, "-------------data packet: elevation=%hd-------\n", elev_angle);

fprintf(ou_fp,"packet_code = %hd\n", packet_code);

fprintf(ou_fp, "packet_len = %d\n", packet_len);

fprintf(ou_fp, "elev_angle = %hd\n", elev_angle);

} /* END of if(offset >0)						*/

} /* END of the while loop 						*/

}

/* close the files opened						*/

fclose(in_fp);

fclose(ou_fp);

}

**********************************************************************

The BURF Fortran Code to create a level 2.5 superob is given below.

C USAGE:    CALL BUFROUT(SUPLAT,SUPLON,HEIT,RWND,RSTD,STDM,RWAZ,NRPTS,

C                        ANEL)

C   INPUT ARGUMENT LIST:

C     SUPLAT   - LATITUDES OF SUPEROBS

C     SUPLON   - LONGITUDES SUPEROBS

C     HEIT     - HEIGHTS OF SUPEROBS ABOVE SEA LEVEL

C     RWND     - RADIAL WIND SUPEROB VALUES

C     RSTD     - STANDARD DEVIATIONS OF SUPEROBS

C     STDM     - TIME DEVIATIONS FROM BASE VALID TIME

C     RWAZ     - AZIMUTH ANGLES IN DEGREES

C     NRPTS    - NUMBER OF SUPEROBS

C     ANEL     - ELEVATION ANGLE OF RADAR ANTENNA

C

C   INPUT FILES:

C     UNIT 40  - BUFR MNEMONIC TABLE (bufrtab.006)

C

C   OUTPUT FILES:

C     UNIT 71  - BUFR OUTPUT FILE CONTAINING SUPEROBED RADIAL WINDS

C

C ATTRIBUTES:

C   LANGUAGE: FORTRAN 90

C   MACHINE:  IBM CCS

C

C$$$

subroutine bufrout(suplat,suplon,heit,rwnd,rstd,stdm,rwaz,nrpts,

. anel)

character*80 hdrstr,rptstr

character*8  cdata(11),subset

integer*8 valid_time,mfac

real*8 ydata(7,nrpts),xdata(11)

real*8 suplat(nrpts),suplon(nrpts),heit(nrpts),

.       rwnd(nrpts),rstd(nrpts),stdm(nrpts),rwaz(nrpts)

equivalence (xdata,cdata)

common/bufrcon/valid_time,stalat,stalon,staheit,ntimes

data mfac/100/

data lunout/71/,lundx/40/

data hdrstr

$  /'RPID CLAT CLON SELV ANEL YEAR MNTH DAYS HOUR MINU MGPT'/

data rptstr /'STDM SUPLAT SUPLON HEIT RWND RWAZ RSTD'/

msgno=0

call datelen(10)

C  FIRST TIME IN, OPEN OUTPUT BUFR FILE

C  ------------------------------------

if(ntimes.eq.1) call openbf(lunout,'OUT',lundx)

ntimes=ntimes+1

subset = 'NC006002'

iyr=valid_time/1000000

mon=mod(valid_time/10000    ,mfac )

idy=mod(valid_time/100      ,mfac )

ihr=mod(valid_time          ,mfac )

imin=00

C  Figure out how many 500 level superob "pieces" this rpt consists of

C  -------------------------------------------------------------------

itimes=nrpts/500+1

if(nrpts.eq.500)  itimes=1

if(nrpts.eq.1000) itimes=2

if(nrpts.eq.1500) itimes=3

if(nrpts.eq.2000) itimes=4

if(nrpts.eq.2500) itimes=5

if(nrpts.eq.3000) itimes=6

if(nrpts.eq.3500) itimes=7

istart=0

ir=500

do ic=1,itimes  ! loop through each 500 level "piece" and

!  generate a new subset and BUFR message

istart=istart+1

iend=min0(nrpts,ir)

ccccc   print*,'checkpt0 - ic,istart,iend = ',ic,istart,iend

xdata=0.0

msgno=msgno+1

call openmg(lunout,subset,valid_time)

cdata(1)='????    '  ! currently do not have report id

xdata(2)=stalat

xdata(3)=stalon

xdata(4)=staheit

xdata(5)=anel

xdata(6)=iyr

xdata(7)=mon

xdata(8)=idy

xdata(9)=ihr

xdata(10)=imin ! data valid on the hr by definition - min is 0

xdata(11)=msgno

print *, 'For elev. angle ',anel,', store "piece" ',ic,

$   ' from "level" ',istart,' to "level" ',iend

write(*,'("Construct a new subset with header: RPID=",A8,

$   ", CLAT=",F6.2,", CLON=",F7.2,", SELV=",F5.0,", ANEL=",F6.2,

$     ", DATE=",I4.4,4I2.2,", MGPT=",I4)')

$     (xdata(ii),ii=1,5), (nint(xdata(ii)),ii=6,11)

call ufbint(lunout,xdata,11,1,nret1,hdrstr)

ccccc   print *, 'checkpt9b,nret1=',nret1

xdata=0.0

numrpts=0

nrp=0

do i=istart,iend  ! loop through the 500 levels in the "piece

!  each contains a superob value

numrpts=numrpts+1

nrp=nrp+1

ydata(1,nrp)=stdm(i)

ydata(2,nrp)=suplat(i)

ydata(3,nrp)=suplon(i)

ydata(4,nrp)=heit(i)

ydata(5,nrp)=rwnd(i)

ydata(6,nrp)=rwaz(i)

ydata(7,nrp)=rstd(i)

enddo

ccccc   print *, 'ydata=', ydata(2,numrpts), ydata(3,numrpts)

call ufbint(lunout,ydata,7,numrpts,nret2,rptstr)

write(*,'(" number of data ""levels"" processed=",I4)') nret2

ccccc   print *, 'checkpt19,numrpts=',numrpts

call writsb(lunout)

istart=iend

ir=ir+500

enddo

call closmg(lunout)

return

end

# Text boxes

|  | MSW | HALFWORD | LSB |
| --- | --- | --- | --- |
|  | PACKET CODE (=27) |
|  | LENGTH OF PACKET (MSW) |
|  | LENGTH OF PACKET (LSW) |
|  | ELEVATION ANGLE |
|  | LATITUDE (MSW) |
| REPEAT | LATITUDE (LSW) |
| FOR | LONGITUDE (MSW) |
| EACH | LONGITUDE (LSW) |
| SUPEROB | HEIGHT |
| CELL WITH AN AVERAGE RADIAL VELOCITY | AVERAGE RADIAL VELOCITY |
|  | STANDARD DEV. OF AVE. RADIAL VELOCITY |
|  | TIME DEVIATION |
|  | AVERAGE AZIMUTH |