## Slide 1
Tools for applying adaptive mesh refinement and automated tuning to wave model simulations
Richard Gorman1, Jose-Henrique Alves2, Hilary Oliver1
NCEP, 30 November 2017
1National Institute of Water and Atmospheric Research, New Zealand
2SRG/EMC/NCEP/NOAA, NOAA Center for Weather and Climate Prediction, College Park, MD, USA

## Slide 2
Wavewatch on an adaptive grid
Richard Gorman

## Slide 3
2010: Gerris (Stephane Popinet)
Adaptive mesh refinement
Quadtree grid in 2D (octree in 3D)
Applied to various flow problems, e.g. Navier-Stokes equations

## Slide 4
Why adaptive mesh refinement for waves?
Wave models are computationally expensive, and computing resources aren’t infinite,
We can’t afford to have very high resolution everywhere
We need to cover full ocean basins
We can used nested rectangular grids or unstructured meshes to give higher resolution where we know in advance it is needed
With tropical cyclones, we need high spatial resolution, but don’t know in advance where it will be needed

## Slide 5
Gerris + Wavewatch
Gerris
Wavewatch subroutine calls

## Slide 6
Simulating an artificial “cyclone”
Rmax = 100 km
Vmax = ramps up from 0 to 50 m/s after 25 hours, then constant
Centre moving southward at 555 km/day.
No background wind field

## Slide 7
Adaptive mesh (48 hours)
6.5 km
13 km
26 km
52 km
104 km
208 km
Spatial resolution
The mesh is refined according to the estimated truncation error in the significant wave height field

## Slide 8
Artificial “cyclone” simulations
Maximum spatial resolution (km)
26
13
6.5
Computing time (hours)
0.1
1
10
100
Wavewatch
gerris constant
gerris adaptive

## Slide 9
Estimated efficiency in global models
Sample global significant wave height field (1/9/2009 00Z NCEP Analysis)
the corresponding truncation error ε for a 0.352 rectangular mesh. Logarithmic scale, ranging from ε < 1mm (dark blue) to ε > 5cm (dark red).

## Slide 10
Number of cells needed in adaptive and constant grids
Starting with the sample wave height field, we apply the refinement algorithm to meet given truncation error targets
Compare the number of grid cells in the resulting adaptive grid with the corresponding constant-resolution grid
Equivalent resolution (degrees)
0.704
0.352
0.176
0.088
1x104
1x105
1x106
1x107
Number of grid cells
constant
adaptive

## Slide 11
Limitations of Gerris-WW3
Gerris-WW3:
  uses WW3 v2.22 source terms,
  has limited I/O,
  has no handling of ice, subgrid obstruction, reflection, …
Need to bring these features in, and keep up with other developments
Who might use/develop it?
Answer?: build adaptivity into Wavewatch

## Slide 12
Quadtree structures
A “quad” is a square divided into four “child” quadrants
Each of these “children” can itself be a “quad”, and further subdivided, or a “leaf” cell, for which model data are computed.
A standard rectangular grid is a special case
Leaf cells correspond to WW3 seapoint index ISEA

## Slide 13
Inputs on a quadtree grid
Refinement level of the the wave model may be controlled by inputs
Bathymetry
Wind, currents, water level
Handle inputs on independent quadtree structures
Inputs may be defined at multiple refinement levels

## Slide 14
Test simulation : 1st order propagation, adaptive grid
Wind speed
Significant wave height

## Slide 15
Quadtree mesh 1 – refinement level

## Slide 16
Quadtree mesh 1 – UNO2 propagation test

## Slide 17
Quadtree mesh 2 – refinement level

## Slide 18
Quadtree mesh 2 – UNO2 propagation test

## Slide 19
Status:
Code version
  Code development brought into a new branch from the EMC_ww3 trunk
Quadtree adaptive processes
  Modules for quadtree operations
I/O:
  Bathymetry & obstructions from multiple regular grids
  Wind, currents, levels, ice ( ← binary ← netcdf)
  Restart files
  Gridded outputs ( → binary → netcdf)
  Point & track outputs
  Input boundary conditions
  Output boundary conditions

## Slide 20
Status
MPI: coded, but needs testing
Physics:
  First order spatial propagation
  Higher order propagation (UNO2, UQ)
  Subgrid obstructions, including “old” ice physics
  Spectral propagation
  Local source terms
  Reflections
  Bottom scattering
  Mud interactions
  New ice physics